## Slide 1
Extensible YANG Model for YANG-Push Notifications I-D: draft-netana-netconf-notif-envelope-02
A. Huang Feng, INSA-Lyon
P. Francois, INSA-Lyon
T. Graf, Swisscom
B. Claise, Huawei
February 6th 2025

## Slide 2: Extensible YANG model for YANG-Push Notifications Proposal of this I-D
Structure defined as a notification containing
  event-time
  metadata(s)
  notification-contents
Collector
enable-notif-envelope=True
Notification-envelope
Configured Subscriptions
enable-notif-envelope=True
Notification-envelope
Dynamic Subscriptions
JSON example without metadata

## Slide 3: Extensible YANG model for YANG-Push Notifications Proposal of this I-D
YANG Notification structure for YANG-Push Notifications [RFC 8639/8641]
  (1) Option to “opt-in” through a YANG-Push Subscription
  (2) Able to discover the capability of this new header through “ietf-notification-capabilities”
  (3) Extensible header defined in YANG 1.1
  (4) Definition of each encoding (XML, JSON, CBOR)
  (5) Defines the first base extensions (I-D.tgraf-netconf-notif-sequencing)

## Slide 4: Extensible YANG model for YANG-Push Notifications Feedback IETF 121 Dublin
Envelope header is configurable per subscription
  Too complex, suggested to enable it globally [Reshad, Rob]
Let’s simplify, don’t allow configuring “which headers” we want
  Suggested to let the client discover what is supported [Joe]
The envelope need to be a sx:structure [Rob]
Plenty of support of this I-D
  Multiple contributors agreed to implement this I-D

## Slide 5: Extensible YANG model for YANG-Push Notifications Changes since -00
(1) Envelope is enabled and disabled globally
(2) Added Observation Timestamp extension [draft-tgraf-netconf-yang-push-observation-time]
(3) Other changes
  The XML namespace has been changed to “urn:ietf:params:xml:ns:yang:ietf-yp-notification”
  Editorial changes
  “The 'notification-contents' element SHOULD be located at the end of the notification envelope structure.”

## Slide 6: Extensible YANG model for YANG-Push Notifications (1) Enabling the envelope globally
Global RPC “enable-notif-envelope”
  This RPC is the only way to enabling/disabling the envelope
  The node “/sn:subscriptions/enable-notification-envelope” becomes read-only
  The enabling of the envelope MUST be configured before the creation of any dynamic subscriptions
    If any subscriptions exist → “invalid-notification-envelope-config” error

## Slide 7: Extensible YANG model for YANG-Push Notifications (1) Enabling the envelope globally
Collector
RFC5277 Header
Configured Subscriptions
enable-notif-envelope=False
RFC5277 Header
Dynamic Subscriptions
enable-notif-envelope=True
Collector
enable-notif-envelope=False
RFC5277 Header
RFC5277 Header
enable-notif-envelope=True
invalid-notification-envelope-config
Collector
RFC5277 Header
Collector
notif-envelope
Collector
notif-envelope
RFC5277 Header
RFC5277 Header

## Slide 8: Extensible YANG model for YANG-Push Notifications (2) Added Observation Timestamp extension
Timestamp representing
  The time the metrics were polled
  The time the exported event occurred
Extensions to YANG-Push
Impact the following YANG-Push Notification only:
  push-update
  push-change-update
Use same mechanism to get the support of this extension via “/sysc:system-capabilities/notc:subscription-capabilities”
Based on: draft-tgraf-netconf-yang-push-observation-time

## Slide 9: Extensible YANG model for YANG-Push Notifications (3) Other minor changes
The XML namespace has been changed to “urn:ietf:params:xml:ns:yang:ietf-yp-notification”
Editorial changes, improve reading
“The 'notification-contents' element SHOULD be located at the end of the notification envelope structure.”
  Idea: have the header located at the beginning of the message

## Slide 10: Extensible YANG model for YANG-Push Notifications Discussion and open issues
All the YANG notifications or only YANG-Push Notifications? So, far, current scope if fine (YANG-Push)
Should this notification be defined as a “notification” or as a “sx:structure”? sx:structure
XML namespace: which one to use?
  urn:ietf:params:xml:ns:netconf:notification:2.0 → following RFC5277
  urn:ietf:params:xml:ns:yang:ietf-yp-notification → following YANG guidelines
Which notification and subscription extensions should be added?
  Metadata sent by default when the envelope is enabled? Yes, feedback IETF 121
  Hostname and Sequencing? [draft-tgraf-netconf-notif-sequencing]; Added
  Observation time? [draft-tgraf-netconf-yang-push-observation-time]; Added
  Some of the extensions only impact a subset of YANG-Push notifications
    How to deal with this? → Current approach, extend YANG-Push header

## Slide 11: Extensible YANG model for YANG-Push Notifications Discussion and open issues
Thanks Qiufang, Andy, Pierre Francois, and Reshad for the feedback.
Request to raise a poll on February 10th interim and confirm wherever proposed changes reflect the will of the WG.
  (1) Envelope is enabled and disabled globally with RPC call
  (2) enable-notification-envelope default=true
  (3) Observation time as an extension
Kent and Mahesh suggested at IETF 122 to initiate working group adoption call.
Considering that this is the 7th document (including the preceding document) iteration, that 4 major implementations are under way and draft-wilton-netconf-yp-observability build on top of it, the authors request to initiate the working group adoption before IETF 122.
We will integrate todays feedback on the next iteration

## Slide 12: BACKUP

## Slide 13: YANG model for NETCONF Event Notifications Interim 2024-09-19 – draft-ahuang-netconf-notif-yang
https://datatracker.ietf.org/doc/minutes-interim-2024-netconf-02-202409191300/
Thorough review of draft-ahuang-netconf-notif-yang/YANG-Push/NETCONF Event Notifications
Conclusion
  draft-ahuang-netconf-notif-yang fixes a gap for YANG-Push but might be worth putting the effort on a brand new header
  We need:
    Bypass RFC5277, thus use YANG-Push only
    Extensible header
      be able to add new metadata (sequencing, versioning, others…)
    A client should be able to “opt-in”
      Clients that don’t support this new header should continue working seamlessly
    The notification should be a YANG-based solution
    Fix JSON and CBOR underspecification
      including CBOR-SID allocation

## Slide 14: YANG model for NETCONF Event Notifications Problem statement - (draft-ahuang-netconf-notif-yang)
<notification xmlns="urn:ietf:params:xml:ns:netconf:notification:1.0">
<eventTime>2022-09-02T10:59:55.32Z</eventTime>
<push-update xmlns="urn:ietf:params:xml:ns:yang:ietf-yang-push">
<id>101</id>
<datastore-contents>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>eth0</name>
<oper-status>up</oper-status>
</interface>
</interfaces>
</datastore-contents>
</push-update>
</notification>
{
"ietf-notification:notification": {
"eventTime": "2017-10-25T08:00:11.22Z",
"ietf-yang-push:push-update": {
"id": 1011,
"datastore-contents": {
"ietf-interfaces:interfaces": [
"interface": {
"name": "eth0",
"oper-status": "up"
}
]
}
}
}
}
RFC 5277 - Netconf Event Notifications
RFC 8641 - YANG Push
YANG encodings:
RFC 7950 - YANG XML
RFC 7951 - YANG JSON
RFC 9254 - YANG CBOR
Implementation Issues:
(1) YANG module not defined
(2) Non-existing Normative text defining this header
Thanks Andy for confirming the approach was not correct.

## Slide 15: Extensible YANG model for YANG-Push Notifications Proposal (comments)
As requested
  Scoped to YANG-Push (both dynamic and configured subscriptions)
    Can be implemented with NETCONF and RESTCONF
  Use a “notification” statement rather than a “sx:structure”
  Given that it’s intended for YANG-Push, the following notifications are impacted:
    push-update; push-change-update
    subscription-started; subscription-modified; subscription-terminated
    subscription-suspended; subscription-resumed; subscription-completed
    replay-completed

## Slide 16: Extensible YANG model for YANG-Push Notifications (1) Option to “opt-in” through a YANG-Push Subscription
Configuration on Globally on the server via the RPC “enable-notif-envelope”
Collector
enable-notification-envelope=true
New envelope Header
Collector
enable-notification-envelope=false
Old Header as RFC5277
Currently
Default=False

## Slide 17: Extensible YANG model for YANG-Push Notifications (2) Able to discover the capability of this new header
Augmentation on notification capabilities (RFC9196)
Get Capabilities
notification-envelope=True

## Slide 18: Extensible YANG model for YANG-Push Notifications (3) Extensible header defined in YANG
Structure defined as a notification containing
  event-time
  metadata(s)
  notification-contents
Collector
enable-notif-envelope=True
Notification-envelope
Configured Subscriptions
enable-notif-envelope=True
Notification-envelope
Dynamic Subscriptions
JSON example without metadata

## Slide 19: Extensible YANG model for YANG-Push Notifications (4) Definition of each encoding (XML, JSON, CBOR)
Explicit definition of the content of the “envelope” (solving gap for JSON and CBOR)
  Definition of the namespace (urn:ietf:params:xml:ns:netconf:notification:2.0)
  Mandatory event-time node
  Mandatory notification-contents node
  Metadata present when configured

## Slide 20: Extensible YANG model for YANG-Push Notifications (5) Extensions for hostname and sequence-number
Definition of hostname and sequence-number extensions (draft-tgraf-netconf-notif-sequencing)
  Present by default when the envelope is enabled
  Discovery of support of this header through RFC9196