## Slide 1: Validate Configured Subscription YANG-Push Publisher Implementations NETCONF & NMOP WG
IETF 119
March 16-17th, 2024
Hackathon

## Slide 2: Hackathon – Plan, Software, Repo
Plan
Validate work in progress vendor YANG-Push publisher implementations.
Configure RFC 8641 compliant YANG-Push configured subscription.
Verify output in packet capture before YANG-Push receiver and after transformation.
Software
6WIND VSR 3.8
Huawei VRP 8.230 C10SPC305T
Pmacct 1.7.10 (20240314.1.7fae9b2-1.el8)
Test Repository
https://github.com/network-analytics/ietf-network-analytics-document-status/tree/main/119/Hackathon

## Slide 3: An Architecture for YANG-Push to Apache Kafka Integration draft-netana-nmop-yang-kafka-integration
Subscription to YANG Notifications for Datastore Updates RFC 8641
UDP-based Transport for Configured Subscriptions draft-ietf-netconf-udp-notif
Subscription to Distributed Notifications draft-ietf-netconf-distributed-notif
Support of Hostname and Sequencing in YANG Notifications draft-tgraf-netconf-notif-sequencing
Support of Versioning in YANG Notifications Subscription draft-ietf-netconf-yang-notifications-versioning
Support of Network Observation Timestamping in YANG Notifications draft-tgraf-netconf-yang-push-observation-time
YANG Library RFC 8525
Augmented-by Addition into the IETF-YANG-Library draft-lincla-netconf-yang-library-augmentation
+------------------------------------------------------------+
| Time Series Database |
+------------------------------------------------------------+
^
| (11) Ingest Data
| According to Schema
+------------------------------------------------------------+
| Time Series Database Ingestion |
+------------------------------------------------------------+
(9) Get | ^ ^ (8) Validate Kafka Message
Schema | | | Against Schema on Consumer
| | |
| | |
| | (10) Issue | (7) Produce Kafka Message
v | Schema (5) Post | with Schema ID prefixed
+--------------------+ Schema +--------------------+
| YANG | <-------------- | Data Collection |
| Schema Registry | --------------> | YANG-Push Receiver |
+--------------------+ (6) Issue +--------------------+
Schema ID (3) Get | ^ (2) Receive YANG-Push
Schema | | Subscription Start Message
| | ^
| | |
| | | (4) Publish YANG-Push
v | | Message with Subscription ID
+--------------------+ +--------------------+
| Network | (1) Subscribe | Network Node |
| Orchestration | ---------------> | YANG-Push Publisher|
+--------------------+ +--------------------+
Figure 1: End to End Workflow

## Slide 4
YANG-Push Data Processing Pipeline
{
"ietf-subscribed-notifications:notification": {
"eventTime": "2024-03-08T16:20:03.520570812+00:00",
"sysName": "daisy-ietf-ipf-zbl1843-r-daisy-58",
"publisherId": 0,
"sequenceNumber": 1502,
"ietf-subscribed-notifications:subscription-terminated": {
"id": 12345678,
"reason": "no-such-subscription"
}
}
}
YANG Push JSON
Apache Kafka
JSON Message
YANG-Push Publisher
YANG-Push Receiver
Apache Kafka

## Slide 5: Subscription Started Notifications (1)
Support of Hostname and Sequencing in YANG Notifications, draft-tgraf-netconf-notif-sequencing, extends the NETCONF notification defined in RFC5277 with sysName, publisherId and sequenceNumber.
{
"ietf-subscribed-notifications:notification": {
"eventTime": "2024-03-08T16:10:02.175903116+00:00",
"sysName": "daisy-ietf-ipf-zbl1843-r-daisy-58",
"publisherId": 0,
"sequenceNumber": 1481,
"ietf-subscribed-notifications:subscription-started": {
"id": 12345678,
"ietf-yang-push:datastore": "ietf-datastores:operational",
"ietf-yang-push:datastore-xpath-filter": "/state/vrf/interface/physical[name='ens192']/counters",
"transport": "ietf-udp-notif-transport:udp-notif",
"encoding": "encode-json",
"purpose": "send notifications",
"ietf-yang-push:periodic": {
"period": 3000
}
}
}
}

## Slide 6: Subscription Started Notifications (2)
Support of Versioning in YANG Notifications Subscription, draft-ietf-netconf-yang-notifications-versioning, adds the ability to subscribe to a specific revision or latest-compatible-semversion. Extends the YANG-Push Subscription State Change Notifications so that the receiver learns on top of xpath and the sub-tree filter also the YANG module name, revision and revision-label.
{
"ietf-notification:notification": {
"eventTime": "2024-03-12T23:20:24Z",
"ietf-subscribed-notification:subscription-started": {
"id": 1,
"ietf-yang-push:datastore": "ietf-datastores:operational",
"ietf-yang-push:datastore-xpath-filter": "/ifm:ifm/ifm:interfaces/ifm:interface",
"ietf-yang-push-revision:revision": "2024-01-23",
"ietf-yang-push-revision:module-name": "ifm",
"ietf-yang-push-revision:revision-label": "1.0.0",
"ietf-distributed-notif:message-observation-domain-id": [1,2],
"transport": "ietf-udp-notif-transport:udp-notif",
"encoding": "encode-json",
"ietf-yang-push:periodic": {
"ietf-yang-push:period": 60000
}
}
}
}

## Slide 7: Push Update Notifications
Support of Hostname and Sequencing in YANG Notifications, draft-tgraf-netconf-notif-sequencing, extends the NETCONF notification defined in RFC5277 with sysName, publisherId and sequenceNumber.
{
"ietf-subscribed-notifications:notification": {
"eventTime": "2024-03-08T16:10:32.161541885+00:00",
"sysName": "daisy-ietf-ipf-zbl1843-r-daisy-58",
"publisherId": 0,
"sequenceNumber": 1482,
"ietf-yang-push:push-update": {
"id": 12345678,
"datastore-contents": {
"vrouter:state": {
"vrf": [
{
"name": "main",
"vrouter-interface:interface": {
"physical": [
{
"name": "ens192",
"counters": {
"in-octets": "8150384",
"in-unicast-pkts": "21684",
"in-discards": "17266",
"in-errors": "0",
"out-octets": "35215236",
"out-unicast-pkts": "392099",
"out-discards": "0",
"out-errors": "0"
}
}

## Slide 8: Push Change Update Notifications
Support of Hostname and Sequencing in YANG Notifications, draft-tgraf-netconf-notif-sequencing, extends the NETCONF notification defined in RFC5277 with sysName, publisherId and sequenceNumber.
Support of Network Observation Timestamping in YANG Notifications, draft-tgraf-netconf-yang-push-observation-time, extends YANG-Push push-update notifications with observation-time and state-changed-observation-time.
{
"ietf-subscribed-notifications:notification": {
"eventTime": "2024-03-08T16:34:07.776844449+00:00",
"sysName": "daisy-ietf-ipf-zbl1843-r-daisy-58",
"publisherId": 0,
"sequenceNumber": 1515,
"ietf-yang-push:push-change-update": {
"id": 12345678,
"datastore-changes": {
"yang-patch": {
"patch-id": "patch-4",
"edit": [
{
"edit-id": "edit-1",
"operation": "replace",
"target": "/vrouter:state/vrf[name='main']/l3vrf[name='A9']/vrouter-interface:interface/vrouter-loopback:loopback[name='Loopback-A9']/enabled",
"value": {
"vrouter-loopback:enabled": true
}
}
]
}
},
"ietf-yang-push-netobs-timestamping:state-changed-observation-time": "2024-03-08T16:34:07.776739137+00:00"
}
}
}

## Slide 9: YANG-Push Implementation Status
 | 6WIND VRP | Huawei VSR | Cisco IOS XR
RFC 8641 YANG-Push | x | x | 
draft-ietf-netconf-udp-notif | x | x | 
draft-ietf-netconf-distributed-notif | x | x | 
draft-ietf-netconf-yang-notifications-versioning |  | x | 
draft-tgraf-netconf-notif-sequencing | x |  | 
draft-tgraf-netconf-yang-push-observation-time | x |  | 
RFC 7895 YANG Module Library |  | x | 
RFC 8525 YANG Library | x |  | x
draft-lincla-netconf-yang-library-augmentation |  |  | 

## Slide 10: Thanks to…
Samuel Gauthier – 6WIND (remote)
Liu Bin – Huawei (remote)
Benoit Claise - Huawei
Paolo Lucente - Pmacct
Yannick Buchs – Swisscom (remote)
Thomas Graf - Swisscom