## Slide 1: Validate YANG-Push to Message Broker End-To-End Data Processing Chain IETF 126 Hackathon, July 18/19th 2026
NMOP & NETCONF WG

## Slide 2: Hackathon Plan, Software and Website
Test Plan
Validate and verify
5 YANG-Push Publishers
2 YANG-Push Receivers
2 YANG-Push Network Telemetry Message
1 YANG Message Broker Producer and Schema Registry
3 YANG Message Broker Consumers
implementation in YANG data integration automation. Subscribe to YANG data on YANG-Publisher, obtain and register all YANG modules necessary to build YANG schema tree, register YANG schemas to Schema Registry and verify YANG notifications against scheme trees and produce and consume from Message Broker.
Software
YANG-Push Publisher - Cisco IOS XR, 6WIND VSR, Huawei NE (Router),MA (OLT), Arrcus Arcos and Ductus DMAP
YANG-Push Receiver – NetGauze® and Pmacct
YANG Message Broker Producer – NetGauze®
YANG Message Broker Consumer – NetGauze®, Ciena Blue Planet UAA Workflow Engine, Cisco Crosswork Ingestion Service
YANG Schema Registry – Apache Kafka YANG Plugin
Libyang - https://github.com/CESNET/libyang/releases/tag/v5.4.9
Yangkit - https://github.com/yang-central/yangkit/
Wireshark - udp-notif dissector
https://www.network-analytics.org/yp/how-to-deploy.html
NMOP & NETCONF WG

## Slide 3: Hackathon – Repositories
The results of the end-to-end tests
Netconf RPCs and YANG-Push JSON and CBOR encoded notifications with wire captures from receiver
YANG-Push Receiver cache content generation with YANG library context, YANG modules, metadata and notification schema validation logs
YANG Message Broker Producer serialization logs
YANG Schema Registry schema examples
YANG Message Broker Consumer, serialization logs, YANG library context, YANG modules and message schema validation
NMOP & NETCONF WG
https://github.com/network-analytics/ietf-network-analytics-document-status/tree/main/126/Hackathon/

## Slide 4: An Architecture for YANG-Push to Message Broker Integration draft-ietf-nmop-yang-message-broker-integration draft-ietf-nmop-message-broker-telemetry-message draft-ietf-nmop-yang-message-broker-message-key draft-netana-nmop-message-broker-bmp-telemetry-message
NMOP & NETCONF WG
Subscription to YANG Notifications RFC 8639
Subscription to YANG Notifications for Datastore Updates RFC 8641
UDP-based Transport for Configured Subscriptions draft-ietf-netconf-udp-notif
Subscription to Distributed Notifications draft-ietf-netconf-distributed-notif
Extensible YANG Model for YANG-Push Notifications draft-ietf-netconf-notif-envelope
Support of Versioning in YANG Notifications Subscription draft-ietf-netconf-yang-notifications-versioning
YANG Modules Describing Capabilities for Systems and Datastore Update Notifications RFC 9196
YANG Notification Transport Capabilities draft-ietf-netconf-yp-transport-capabilities
YANG Library RFC 8525
Augmented-by Addition into the IETF-YANG-Library draft-ietf-netconf-yang-library-augmentation
Validating anydata in YANG Library context draft-netana-nmop-yang-anydata-validation
Encoding of Data Modeled with YANG in the CBOR RFC 9254
+------------------------------------------------------------+
| Data Storage |
+------------------------------------------------------------+
^
| (12) Ingest Data
| According to Schema
+------------------------------------------------------------+
| Data Consumer |
+------------------------------------------------------------+
| ^ ^
(10) Get | | | (9) Validate
Schema | | | Serialized Message
| | | Schema on Consumer
| | +--------------------+
| | | Message |
| | | Broker |
| | +--------------------+
| | ^
| | | (8) Serialize
| | (11) Issue | YANG-Push Message
| | Schema | annotated Schema
v | (6) Post | ID on Producer
+--------------------+ Schema +--------------------+
| YANG | <--------------- | Data Collection |
| Schema Registry | ---------------> | YANG-Push Receiver |
+--------------------+ (7) Issue +--------------------+
| Schema ID | ^ (3) Receive
| | | YANG-Push
v (4) Discover | | Subscription
+--------------------+ Schema | | Start Message
| Stream | Dependencies | | ^
| Catalog | and Obtain | | | (5) Publish
+--------------------+ Schemas | | | YANG-Push
| | | Message
| | | with
(1) Discover | | | Subscriber
Notification v | | ID
+--------------------+ Capabilities +--------------------+
| Manage YANG-Push | ---------------> | Network Node |
| Subscription | ---------------> | YANG-Push Publisher|
+--------------------+ (2) Subscribe +--------------------+

## Slide 5: YANG-Push Publisher - Subscription
NMOP & NETCONF WG
Netconf RPC calls to create, delete and obtain YANG-Push subscriptions and receiver configurations.

## Slide 6: YANG-Push Publisher - Notifications
NMOP & NETCONF WG
Subscription state change notifications as JSON and PCAP.
Push update and change-update notifications as JSON and PCAP.

## Slide 7: YANG-Push UDP-Notif – DTLS and CBOR
NMOP & NETCONF WG
With Cisco IOS XR, 6Wind VSR and Arrcus Arcos we have now three implementations support CBOR Name Identifiers
With Cisco IOS XR we have the first implementation support DTLS 1.2 in UDP-Notif.

## Slide 8: YANG-Push Capabilities & YANG Library - RPC
NMOP & NETCONF WG
Netconf XML encoded reply for RFC 9196 YANG-Push capabilities.
Netconf XML encoded reply for RFC 8525 with draft-ietf-netconf-yang-library-augmentedby.

## Slide 9
NMOP & NETCONF WG
YANG-Push IETF 126 Publisher Implementation Status
 | 6WIND VSR | Huawei NE | Huawei MA | Cisco IOS XR | Arrcus Arcos | Open-Source | Ductus DMAP
RFC 8639 YANG-Push Subscription | ✔ | ✔ | ✔ | ✔ | ✔ |  | ✔
RFC 8641 YANG-Push Notification | ✔ | ✔ | ✔ | ✔ | ✔ |  | ✔
draft-ietf-netconf-udp-notif | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | 
draft-ietf-netconf-udp-notif with DTLS |  |  |  | ✔ |  |  | 
draft-ietf-netconf-distributed-notif | ✔ | ✔ | ✔ |  | na |  | 
draft-ietf-netconf-notif-envelope | ✔ | ✔ | ✔ | ✔ | ✔ |  | P
draft-ietf-netconf-yang-notifications-versioning | ✔ | ✔ | ✔ | ✔ | ✔ |  | 
RFC 8525 YANG Library | ✔ | ✔ | ✔ | ✔ | ✔ |  | ✔
draft-ietf-netconf-yang-library-augmentation | ✔ | ✔ | ✔ | ✔ |  | ✔ | ✔
RFC 9196 System and Notification Capabilities |  |  | ✔ | P | ✔ |  | ✔
draft-netana-netconf-yp-transport-capabilities |  |  | ✔ | ✔ | ✔ |  | 
RFC 9254 CBOR Named Identifiers | ✔ |  |  | ✔ | ✔ |  | 
Green marked describes new capability at IETF 126. "P" to partially implemented.

## Slide 10
NMOP & NETCONF WG
Operational IETF/IEEE YANG IETF 126 Module Implementation Status
Green marked describes new capability at IETF 126. "P" to partially implemented.
 | 6WIND VSR | Huawei NE | Huawei MA | Cisco IOS XR | Arrcus Arcos
ietf-interfaces.yang (inventory, state and statistic) | ✔ | ✔ | ✔ |  | 
ietf-hardware.yang (inventory, state and statistic) | ✔ | ✔ | ✔ |  | 
ietf-alarms.yang (state) | ✔ | ✔ | ✔ |  | 
ieee802-dot1ab-lldp.yang (inventory and state) | ✔ | ✔ |  |  | 
ieee802-dot1ax.yang (inventory, state and statistic) |  |  |  |  | 
ietf-bfd-ip-sh.yang (state) |  |  |  |  | 
ietf-bfd-ip-mh.yang (state) |  |  |  |  | 
ietf-bfd-lag.yang (state) |  |  |  |  | 
ietf-isis.yang (state) |  |  |  |  | 

## Slide 11
NMOP & NETCONF WG
YANG Message Broker IETF 126 Implementation Status
Green marked describes new capability at IETF 126. "P" to partially implemented.
 | NetGauze® | Pmacct | Apache Kafka | Ciena Blueplanet | Cisco Crosswork
draft-ietf-nmop-message-broker-telemetry-message | ✔ | ✔ |  |  | 
YANG-Push Receiver | ✔ | ✔ |  |  | 
YANG Schema Retrieval | ✔ |  |  |  | 
YANG Message Broker Producer | ✔ |  |  |  | 
YANG Schema Registry | na | na | ✔ | na | na
YANG Message Broker Consumer | ✔ |  |  | ✔ | ✔
Validate Telemetry Message against YANG Schema | ✔ |  |  | P | P
draft-ietf-netmod-yang-anydata-validation | ✔ |  |  |  | 
YANG Schema Comparison | na | na | ✔ | na | na

## Slide 12: YANG Library Feature Comparison
NMOP & NETCONF WG
An extensive YANG feature comparison between the different YANG library open-source implementations.
Focuses on YANG features needed to validate YANG instance data against YANG schema and performing YANG to YANG transformations.
https://github.com/network-analytics/yang_tests/blob/master/report_v2.pdf

## Slide 13: Next Steps from IETF 125 Hackathon…
Re-do YANG Message Broker Consumer tests on updated testbed with Ciena Blue Planet UAA Workflow Engine
Complete IETF YANG module subscription tests with 6Wind VSR
Compare YANG feature coverage between libyang, yangkit and yangtools
Revert import only modules for augmented-by workaround
Preserve cached YANG-Push subscription state across receiver reload
Obtain YANG-Push subscription state from publisher if missing
Support Netconf session queuing for schema retrieval
Support libyang 5.4.9 in YANG-Push Receiver and Message Broker Consumer
Message Key and Topic Name proof of concept
NMOP & NETCONF WG

## Slide 14: Next Steps for IETF 127 Hackathon…
Support building RFC 8525 YANG Library in Java Message Broker Consumer
Support draft-netana-nmop-yang-anydata-validation and RFC 8525 YANG library in yangkit
Support YANG-Push Message Broker Topic Naming with dynamic Apache Kafka topic creation API
NMOP & NETCONF WG

## Slide 15: Thanks to…
Jiaxin PAN – Huawei
Zhengliang Li – Huawei
Xiao Chen - Huawei
Rob Wilton – Cisco
Dan Voyer – Cisco
Muthumayan Madhayyan - Cisco
Jérémie Leska – 6Wind
Per Anderson - Ductus
Deepya Mandadi – Ciena
Sivakumar Sundaravadivel – Ciena
IJsbrand Wijnands – Arrcus
Irfan Mohammad – Arrcus
Benoit Claise - Everything OPS
Paolo Lucente – Pmacct
Vivekananda Boudia – INSA Lyon
Alex Huang Feng – INSA Lyon/T-Systems
Maxence Younsi – INSA Lyon/Swisscom
Ashvanth Kumar Selvakumaran - Telus
Leonardo Rodoni - Swisscom
Ahmed Elhassany – Swisscom
Thomas Graf – Swisscom
NMOP & NETCONF WG
Want to know more then join us at…
NMOP on Monday 09:00 – 11:00 at the Grand Klimt Hall 2 for Message Broker, Message Key, BMP Telemetry Message document updates and hackathon related details.
NETMOD on Thursday 09:00 – 11:00 at the Grand Klimt Hall 1 for YANG Library feature comparison related details.