## Slide 1
An Architecture for a Network Anomaly Detection Framework draft-netana-nmop-network-anomaly-architecture-00
Motivation and architecture of a Network Anomaly Detection Framework
and the relationship to other documents describing
network symptom semantics and network incident lifecycle
wanting.du@swisscom.com pierre.francois@insa-lyon.fr
thomas.graf@swisscom.com vincenzo.riccobene@huawei-partners.com
09. July 2024

## Slide 2: Data Mesh organizes Data in Organizations Enables Network Analytics use cases
Network Data Collection
Network Device Trend Detection
Verify, Troubleshoot and Notify
Closed Loop Operation
Network Anomaly Detection
Network Visualization
Network SLI and SLO
Alert
Postmortem
Operational Data
draft-netana-nmop-network-anomaly-semantics draft-netana-nmop-network-anomaly-lifecycle
RFC 8632
Analytical Data
Network Telemetry
RFC 9232
draft-netana-nmop-network-anomaly-architecture

## Slide 3: What to monitor Which operational metrics are collected
« Network operators connect customers in routing tables called Connectivity Services »
« Network Telemetry (RFC 9232) describes how to collect data from all 3 network planes efficiently »

## Slide 4: What does Network Anomaly Detection mean Monitor changes, called outliers, in networks
Network Anomaly Detection
For Connectivity Services, Network Anomaly Detection constantly monitors and detects any network or device topology change, along with their associated forwarding consequences for customers as outliers. Notifications are sent to the Network Operation Center before the customer is aware of service disruptions. It offers operational metrics for in-depth analysis, allowing to understand in which platform the problem originates and facilitates problem resolution.
Answers
What changed and when, on which connectivity service, and how does it impact the customers?
Focuses
Provides meaningful connectivity service impact information before customer is aware of and support in root-cause analysis.
Data Mesh
Consumes operational real-time Forwarding Plane, Control Plane and Management Plane metrics and produces analytical alerts.
Direction
From connectivity service to network platform.

## Slide 5: What our motivation is Automate learn and improve
From network incidents postmortems we network operators learn and improve so does network anomaly detection and supervised and semi-supervised machine learning.
The more network incidents are observed, the more we can improve. With more incidents the postmortem process needs be automated, let's get organized first by defining human and machine-readable metadata semantics and annotate operational and analytical data.
Let's get further organized by exchanging standardized labeled network incident data among network operators, vendors and academia to collaborate on academic research.
« The community working on Network Anomaly Detection is probably the only group wishing for more network incidents »

## Slide 6: Elements of the Architecture
Service Inventory contains list of the connectivity services.
Service Disruption Detection processes aggregated network data to decide whether a service is degraded or not.
Service Disruption Detection Configuration defines the set of approaches that need to be applied to perform SDD.
Operational Data Collection manages network telemetry subscriptions and transforms data into message broker.
Operational Data Aggregation produces data upon which detection of a service disruption can be performed.
Network Modeling establishes knowledge of network relationships.
Data Profiling categorizes nondeterministic customer related data.
Detection Strategies for a profile a detection strategy is defined.
Machine Learning is commonly used to detect outliers or anomalies.
Storage some algorithms may relay on historical (aggregated) operational data to detect anomalies.
Alerting consolidates analytical insights and notifies.
Postmortem refines and stores the network anomaly and symptom labels into the Label Store.
Replaying to validate refined anomaly and symptom labels, historical operational data is replayed.

## Slide 7: Experiment: Network Anomaly Lifecycle draft-netana-nmop-network-anomaly-lifecycle
Detection: The Network Anomaly Detection stage is about the continuous monitoring of the network through Network Telemetry [RFC9232] and the identification of symptoms.
Validation: Decides if the detected symptoms are signaling a real incident or if they are to be treated as false positives.
Refinement: Network operator performs detailed postmortem analysis of the network incident, collected Network Telemetry data and detected anomaly with the objective to identify useful adjustments in the Network Telemetry data collection and Anomaly Detection system.

## Slide 8: Semantic Metadata Annotation for Network Anomaly Detection draft-netana-nmop-network-anomaly-semantics
module: ietf-network-anomaly-metadata
+--rw network-anomalies
+--rw network-anomaly* [id author-name version state]
+--rw id yang:uuid
+--rw description? string
+--rw author
| +--rw author-name string
| +--rw author-type? identityref
| +--rw algo-version? uint8
+--rw version uint8
+--rw state identityref
+--rw symptoms* [symptom_id]
+--rw symptom_id yang:uuid
ID and Description uniquely identifies the detected anomaly.
Author Name, Type, Version and Algo-Version describes wherever the anomaly was detected by a human or algorithm and uniquely identifies the system and version who/which detected.
State describes the state of the anomaly (selected among the states defined in the state machine).
Symptoms describes the identified symptoms defined in ietf-symptom-semantic-metadata.

## Slide 9: An Architecture for a Network Anomaly Detection Framework Status, Summary and Next steps
Status of draft-netana-nmop-network-anomaly-architecture-00
Initial document published. Requesting feedback from the working group.
Status of draft-netana-nmop-network-anomaly-semantics-02 and draft-netana-nmop-network-anomaly-lifecycle-03
Referred to draft-netana-nmop-network-anomaly-architecture as the main document for the architecture
Change the term source to annotator and updated the YANG modules accordingly
Added/updated terminology section with references to draft-ietf-nmop-terminology and draft-netana-nmop-network-anomaly-architecture
Moved data mesh and outlier detection section to draft-netana-nmop-network-anomaly-architecture
Next Steps
Request adoption for all 3 documents starting with draft-netana-nmop-network-anomaly-architecture-00.
In-depth coverage at NMOP interim meeting on September 11th.

## Slide 10: Relevant Papers for more Details
Paper “Daisy: Practical Anomaly Detection in large BGP/MPLS and BGP/SRv6 VPN Networks” published at ACM/IRTF ANRW’23
San Francisco, USA (24 July 2023)
Open access: http://hal.science/hal-04307611
Paper “Practical Anomaly Detection in Internet Services: An ISP centric approach”
accepted at AnNet’24
(in conjunction with IEEE NOMS’24)
Seoul, Korea (6–10 May 2024)
[Will be presented as a poster the May 6th 2024]