## Slide 1
Semantic Metadata Annotation for Network Anomaly Detection draft-netana-nmop-network-anomaly-semantics-01
Experiment: Network Anomaly Lifecycle draft-netana-nmop-network-anomaly-lifecycle-01
Helps to annotate operational data, refine outlier detection, supports supervised and semi-supervised machine learning development,
enables data exchange among network operators, vendors and academia, and make anomalies for humans apprehensible
thomas.graf@swisscom.com wanting.du@swisscom.com
alex.huang-feng@insa-lyon.fr
vincenzo.riccobene@huawei-partners.com
antonio.roberto@huawei.com
12. March 2024

## Slide 2: What to monitor Which operational metrics are collected
« Network operators connect customers in routing tables called VPN's »
« Network Telemetry (RFC 9232) describes how to collect data from all 3 network planes efficiently »

## Slide 3: How to organize and collaborate with data The Data Mesh Architecture enables Network Analytics use
Network Data Collection
Network Device Trend Detection
Verify, Troubleshoot and Notify
Closed Loop Operation
Network Anomaly Detection
Network Visualization
Network SLI and SLO
Alert
Postmortem
Operational Data
draft-netana-nmop-network-anomaly-semantics draft-netana-nmop-network-anomaly-lifecycle
RFC 8632
Analytical Data
RFC 9232

## Slide 4: What our motivation is Automate learn and improve
From network incidents postmortems we network operators learn and improve so does network anomaly detection and supervised and semi-supervised machine learning.
The more network incidents are observed, the more we can improve. With more incidents the postmortem process needs be automated, let's get organized first by defining human and machine-readable metadata semantics and annotate operational and analytical data.
Let's get further organized by exchanging standardized labeled network incident data among network operators, vendors and academia to collaborate on academic research.
« The community working on Network Anomaly Detection is probably the only group wishing for more network incidents »

## Slide 5: Postmortem, Maximum Prefix BGP Peer State Change SBInfo-028166, PBI000000193943, INC000012284550
IPFIX configured on PE and Inter-AS Option A ASBR nodes.
Traffic Drop with Reason Code Adjacency at TV was unrelated.
BMP ADJ-RIB In pre-policy on BGP VPNv4 /6 and IPv4/6 VRF unicast peers configured on MPLS PE's. BMP ADJ-RIB In pre-policy on BGP VPNv4 /6 on Route Reflectors.
BMP peer_down reports that it is type 4 (Remote system closed, no data) instead of type 1 (Local system closed, NOTIFICATION PDU follows) due to CSCwi61922.
Missing Traffic 64497:6
Flow Count Drop 64497:6
BMP Peer State Change 64497:6
Traffic Drop 64497:6

## Slide 6: Postmortem, Maximum Prefix BGP Peer State Change SBInfo-028166, INC000012284550, Bright Lights Live
BMP route-monitoring Update/Withdraw recognized topology change.
BMP peer Down recognized peering state change delayed due to potential data processing lag.
Interface Down/Up check did not apply.
Traffic Drop check recognized forwarding drop.
Missing Traffic recognized that connectivity is impaired.
Flow Count Spike did not apply.
Overall: 4 out of 6 checks have detected a customer impact inside of monitoring domain. Works as designed.
Cosmos Bright Lights Anomaly Detection – 64497:6 SC-DCI
Max Concern Score: 0.36
Traffic Drop: 1.0 Missing Traffic: 0.13
BMP Update/Withdraw: 1.0
BMP Peer Down: 0.76

## Slide 7
What went well?
Anomaly Detection rules detected outage based on BMP update/withdrawal and peer_down, IPFIX flow count drop, traffic drop and missing traffic. Works as designed.
What could be improved?
Consider to implement capacity management and trend detection analytical use case for BGP max prefix configured peers, BGP Local RIB path count and BGP process memory.
draft-ietf-grow-bmp-rel authors considering to support two reason code TLV's for prefixes crossing the warning and the maximum threshold.
draft-msri-grow-bmp-bgp-rib-stats authors contacted at GROW to consider another BMP statistics definition describing how many percent of the configured maximum prefix count has been reached.
Similar as we are draft-ietf-grow-bmp-path-marking-tlv how the BGP path will be installed into the RIB, we could add as a TLV also the local allocated MPLS label from the Label FIB.
BMP peer_down reason code is 4 instead of 1 on Cisco IOS XR. Addressed and confirmed in SR 696692110. CSCwi61922 bugfix verified.
BGP notification sub-code support in NetGauze verified.
Postmortem
What to do next?
Record incident in Cosmos Bright Lights lab. -> Done!
Analyze why (TSDB ingestion delay?) not all BMP peer_down where being recognized by BMP peer_down check.

## Slide 8: What is a symptom and how to categorize them From action to reason to cause
Action: Which action the network node performed for a packet in the forwarding plane, a path or adjacency in the control plane or state or statistical changes in the management plane.
Reason: For each reason one or more actions describing why this action was used. From drop unreachable, administered, and corrupt in forwarding plane, to reachability withdraw and adjacency teared down in control plane, to Interface down, errors or discard in management plane.
Cause: For each reason one or more causes describes why the action was chosen. From missing next-hop and link-layer information in forwarding plane, to reachability withdrawn due to peer down or path no longer redistributed.
« Symptoms are categorized in which plane they have been observed, their action, reason and cause »

## Slide 9: Outliers in Anomaly Detection From global to contextual to collective
Global outliers: An outlier is considered "global" if its behavior is outside the entirety of the considered data set.
Contextual outliers: An outlier is considered "contextual" if its behavior is within a normal (expected) range, but it would not be expected based on some context. Context can be defined as a function of multiple parameters, such as time, location, etc.
Collective outliers: An outlier is considered "collective" if the behavior of each single data point that are part of the anomaly are within expected ranges (so they are not anomalous, it’s either a contextual or a global sense), but the group taking all the data points together, is.
« Collective outliers are important because networks are connected. Through different planes interconnected symptoms from various angles can be observed »

## Slide 10: Annotate Operational Data YANG Module
Symptoms describe what changed in the network for what reason and cause with which concern score from when to when.
Tags describes in which network plane, which action, reason and cause was observed.
Pattern describes the measurement pattern over time of the time series data.
Source describes which system observed the outlier. A human or a network anomaly detection system.
module: ietf-symptom-semantic-metadata
+--rw symptom
+--rw id yang:uuid
+--rw event-id yang:uuid
+--rw description string
+--rw start-timeyang:date-and-time
+--rw end-time yang:date-and-time
+--rw confidence-score float
+--rw concern-score? float
+--rw tags* [key]
| +--rw key string
| +--rw value string
+--rw (pattern)?
| +--:(drop)
| | +--rw dropempty
| +--:(spike)
| | +--rw spike empty
| +--:(mean-shift)
| | +--rw mean-shift empty
| +--:(seasonality-shift)
| | +--rw seasonality-shift empty
| +--:(trend)
| | +--rw trend empty
| +--:(other)
| +--rw other string
+--rw source
+--rw (source-type)
| +--:(human)
| | +--rw human empty
| +--:(algorithm)
| +--rw algorithm empty
+--rw name? string

## Slide 11: Experiment: Network Anomaly Post-mortem Lifecycle What is the Motivation?
Network anomaly detection is about identifying behaviours that provide evidence of consumers experiencing a service degradation.
During our work to implement network anomaly detection, we realized that this requires a continuous review process, in order to iteratively collect and incorporate more and more network and service knowledge into the methodology.
Network operators often implement review processes of their detection mechanisms to improve over time (reducing both False Positives and False Negatives), validating the detected network anomalies and performing post-mortem analysis, etc.
We see the need to provide a well-defined lifecycle for the refinement of network anomaly detection, as this can open up to a more structured cooperation between different actors involved in different stages of the lifecycle, including customer service operators, network engineers, Data Scientists, AI algorithms, etc.
This proposed draft describe an experiment: verifying whether the approach is usable in real use case scenarios to support proper refinement and adjustments of network anomaly detection algorithms.

## Slide 12: Network Anomaly Postmortem Lifecycle draft-netana-nmop-network-anomaly-lifecycle
Detection: The Network Anomaly Detection stage is about the continuous monitoring of the network through Network Telemetry [RFC9232] and the identification of symptoms.
Validation: Decides if the detected symptoms are signaling a real incident or if they are to be treated as false positives.
Refinement: Network operator performs detailed postmortem analysis of the network incident, collected Network Telemetry data and detected anomaly with the objective to identify useful adjustments in the Network Telemetry data collection and Anomaly Detection system.

## Slide 13: Network Anomaly State Machine Incident Relationships
Incident Forecasted: A potential network incident is predicted in the future by the Network Anomaly Detection system.
Incident Potential: A potential network incident has been detected by the Network Anomaly Detection system.
Incident Confirmed: A potential network incident has been confirmed in the postmortem validation.

## Slide 14: Network Anomaly Metadata YANG Module
module: ietf-network-anomaly-metadata
+--rw network-anomalies
+--rw network-anomaly* [id author-name version state]
+--rw id yang:uuid
+--rw description? string
+--rw author
| +--rw author-name string
| +--rw author-type? identityref
| +--rw algo-version? uint8
+--rw version uint8
+--rw state identityref
+--rw symptoms* [symptom_id]
+--rw symptom_id yang:uuid
ID and Description uniquely identifies the detected anomaly.
Author Name, Type, Version and Algo-Version describes wherever the anomaly was detected by a human or algorithm and uniquely identifies the system and version who/which detected.
State describes the state of the anomaly.
Symptoms describes the identified symptoms defined in ietf-symptom-semantic-metadata.

## Slide 15: IETF 119 Hackathon – Antagonist Labelling a Symptom in Grafana
Vertical dotted lines are the tagged symptoms.
Once the symptom is selected, the user can add all the details.
Once the symptom is defined it gets submitted to Antagonist.
1
2

## Slide 16: IETF 119 Hackathon - Antagonist Design and workflow
Antagonist (Anomaly tagging on historical data)
Time Series Database
Symptom Annotation Tool
REST API
Antagonist Frontend
Source Code: https://github.com/vriccobene/antagonist
Telemetry Data
Time Series Metrics
Symptoms & Network Anomalies (+ metadata)
Symptoms & Network Anomalies (+ metadata)
Example:
Example:
Antagonist has been extended to become agnostic of the technologies used for the persistence and annotation of telemetry data
Antagonist exposes a REST API to support ingestion and exposure of symptoms and network anomaly data and semantic metadata.
The exposed data can be used as ground-truth.

## Slide 17: Add Screenshot from Antagonist Frontend

## Slide 18: Semantic Metadata Annotation for Network Anomaly Detection Next steps
This work relates to the Network Anomaly Detection topic in the NMOP charter.
It bridges network and data engineering, operator, vendors and academia, domains by having the semantics and ontology of network symptoms for operational and analytical data defined.
This work will unveil what is missing in Network Telemetry data and provide input to other documents such as draft-davis-nmop-incident-terminology to enable a more detailed and holistic view for networks.
Do you realize the benefit of having standardized semantic metadata annotation for Network Anomaly Detection and how it helps network operators, vendor and academia to collaborate?
-> What are your thoughts and comments?
-> We request NMOP working group adoption.
thomas.graf@swisscom.com wanting.du@swisscom.com
alex.huang-feng@insa-lyon.fr
vincenzo.riccobene@huawei-partners.com
antonio.roberto@huawei.com
12. March 2024

## Slide 19: Experiment: Network Anomaly Lifecycle Next steps
This work relates to the Network Anomaly Detection topic in the NMOP charter.
It defines the Network Anomaly lifecycle by providing a structured way to perform post-mortem analysis iteratively and improve the network anomaly detection methodology.
Our future intention: expanding and validate this approach on real use case scenarios on Swisscom network incident data.
This work will provide input to draft-davis-nmop-incident-terminology and complement other documents such as RFC 8632 and draft-feng-opsawg-incident-management where semantics for alerts and incidents are defined.
Do you realize the benefit of having a defined workflow and semantics to automate the Network Anomaly Lifecycle?
-> What are your thoughts and comments?
thomas.graf@swisscom.com wanting.du@swisscom.com
alex.huang-feng@insa-lyon.fr
vincenzo.riccobene@huawei-partners.com
antonio.roberto@huawei.com
12. March 2024