## Slide 1
Extensible YANG Model for YANG-Push Notifications I-D: draft-netana-netconf-notif-envelope-00
A. Huang Feng, INSA-Lyon
P. Francois, INSA-Lyon
T. Graf, Swisscom
B. Claise, Huawei
November 8th 2024

## Slide 2: Extensible YANG model for YANG-Push Notifications
YANG Notification structure for YANG-Push Notifications
  (1) Option to “opt-in” through a YANG-Push Subscription
  (2) Able to discover the capability of this new header through “ietf-notification-capabilities”
  (3) Extensible header defined in YANG
  (4) Definition of each encoding (XML, JSON, CBOR)
  (5) Extensions for hostname and sequence-number included (I-D.tgraf-netconf-notif-sequencing)

## Slide 3: YANG model for NETCONF Event Notifications Interim 2024-09-19 – draft-ahuang-netconf-notif-yang
https://datatracker.ietf.org/doc/minutes-interim-2024-netconf-02-202409191300/
Thorough review of draft-ahuang-netconf-notif-yang/YANG-Push/NETCONF Event Notifications
Conclusion
  draft-ahuang-netconf-notif-yang fixes a gap for YANG-Push but might be worth putting the effort on a brand new header
  We need:
    Bypass RFC5277, thus use YANG-Push only
    Extensible header
      be able to add new metadata (sequencing, versioning, others…)
    A client should be able to “opt-in”
      Clients that don’t support this new header should continue working seamlessly
    The notification should be a YANG-based solution
    Fix JSON and CBOR underspecification
      including CBOR-SID allocation

## Slide 4: YANG model for NETCONF Event Notifications Problem statement - (draft-ahuang-netconf-notif-yang)
<notification xmlns="urn:ietf:params:xml:ns:netconf:notification:1.0">
<eventTime>2022-09-02T10:59:55.32Z</eventTime>
<push-update xmlns="urn:ietf:params:xml:ns:yang:ietf-yang-push">
<id>101</id>
<datastore-contents>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>eth0</name>
<oper-status>up</oper-status>
</interface>
</interfaces>
</datastore-contents>
</push-update>
</notification>
{
"ietf-notification:notification": {
"eventTime": "2017-10-25T08:00:11.22Z",
"ietf-yang-push:push-update": {
"id": 1011,
"datastore-contents": {
"ietf-interfaces:interfaces": [
"interface": {
"name": "eth0",
"oper-status": "up"
}
]
}
}
}
}
RFC 5277 - Netconf Event Notifications
RFC 8641 - YANG Push
YANG encodings:
RFC 7950 - YANG XML
RFC 7951 - YANG JSON
RFC 9254 - YANG CBOR
Implementation Issues:
(1) YANG module not defined
(2) Non-existing Normative text defining this header
Thanks Andy for confirming the approach was not correct.

## Slide 5: Extensible YANG model for YANG-Push Notifications Proposal (comments)
As requested
  Scoped to YANG-Push (both dynamic and configured subscriptions)
    Can be implemented with NETCONF and RESTCONF
  Use a “notification” statement rather than a “sx:structure”
  Given that it’s intended for YANG-Push, the following notifications are impacted:
    push-update; push-change-update
    subscription-started; subscription-modified; subscription-terminated
    subscription-suspended; subscription-resumed; subscription-completed
    replay-completed

## Slide 6: Extensible YANG model for YANG-Push Notifications (1) Option to “opt-in” through a YANG-Push Subscription
Configuration on a per-subscription basis
Collector
enable-notification-envelope=true
New envelope Header
Collector
enable-notification-envelope=false
Old Header as RFC5277
Currently
Default=False

## Slide 7: Extensible YANG model for YANG-Push Notifications (2) Able to discover the capability of this new header
Augmentation on notification capabilities (RFC9196)
Get Capabilities
notification-envelope=True

## Slide 8: Extensible YANG model for YANG-Push Notifications (3) Extensible header defined in YANG
Structure defined as a notification containing
  event-time
  metadata(s)
  notification-contents
Collector
enable-notif-envelope=True
Notification-envelope
Configured Subscriptions
enable-notif-envelope=True
Notification-envelope
Dynamic Subscriptions
JSON example without metadata

## Slide 9: Extensible YANG model for YANG-Push Notifications (4) Definition of each encoding (XML, JSON, CBOR)
Explicit definition of the content of the “envelope” (solving gap for JSON and CBOR)
  Definition of the namespace (urn:ietf:params:xml:ns:netconf:notification:2.0)
  Mandatory event-time node
  Mandatory notification-contents node
  Metadata present when configured

## Slide 10: Extensible YANG model for YANG-Push Notifications (5) Extensions for hostname and sequence-number
Definition of hostname and sequence-number extensions (draft-tgraf-netconf-notif-sequencing)
  Present by default when the envelope is enabled
  Discovery of support of this header through RFC9196

## Slide 11: Extensible YANG model for YANG-Push Notifications Discussion and open issues
Is this approach the way to go?
All the YANG notifications or only YANG-Push Notifications?
Should this notification be defined as a “notification” or as a “sx:structure”?
XML namespace: which one to use?
  urn:ietf:params:xml:ns:netconf:notification:2.0 → following RFC5277
  urn:ietf:params:xml:ns:yang:ietf-yp-notification → following YANG guidelines
Which notification and subscription extensions should be added?
  Metadata sent by default when the envelope is enabled?
  YANG versioning? [draft-ietf-netconf-yang-notifications-versioning (currently adopted)]
  Observation time? [draft-tgraf-netconf-yang-push-observation-time]
  Some of the extensions only impact a subset of YANG-Push notifications
    How to deal with this?