## Slide 1: Validate Validate Network Telemetry Messages Implementations IETF 124 Hackathon, November 1-2nd 2025
NMOP & NETCONF WG

## Slide 2: Hackathon Plan, Software and Website
Test Plan
Message Broker integration
  Validate draft-ietf-nmop-message-broker-telemetry-message for draft-ietf-nmop-yang-message-broker-integration integration against YANG schema with yanglint
Software
YANG-Push Publisher - Cisco IOS XR
YANG-Push Publisher - 6WIND VSR
YANG-Push Publisher - Huawei NE (Router) and MA (OLT)
YANG-Push Receiver – Netgauze
YANG-Push Receiver – Pmacct
udp-notif dissector - Wireshark
https://www.network-analytics.org/yp/how-to-deploy.html
NMOP & NETCONF WG

## Slide 3: Hackathon – Repositories
YANG-Push Test Result Repository
https://github.com/network-analytics/ietf-network-analytics-document-status/tree/main/123/Hackathon
  Packet capture on the wire
  Netconf RPCs and YANG-Push JSON and CBOR encoded messages
Telemetry Message Test Result Repository
https://github.com/network-analytics/ietf-network-analytics-document-status/tree/main/124/Hackathon
  Pmtelemetryd configuration and JSON telemetry messages
  YANG schemas for validation
Apache Kafka Integration
https://github.com/network-analytics/yang-kafka-integration
  YANG Serializer
  YANG Schema Registry Plugin
NMOP & NETCONF WG

## Slide 4: An Architecture for YANG-Push to Message Broker Integration draft-ietf-nmop-yang-message-broker-integration draft-ietf-nmop-message-broker-telemetry-message draft-netana-nmop-yang-message-broker-message-key
NMOP & NETCONF WG
Subscription to YANG Notifications RFC 8639
Subscription to YANG Notifications for Datastore Updates RFC 8641
UDP-based Transport for Configured Subscriptions draft-ietf-netconf-udp-notif
Subscription to Distributed Notifications draft-ietf-netconf-distributed-notif
Extensible YANG Model for YANG-Push Notifications draft-ietf-netconf-notif-envelope
Support of Versioning in YANG Notifications Subscription draft-ietf-netconf-yang-notifications-versioning
YANG Modules Describing Capabilities for Systems and Datastore Update Notifications RFC 9196
YANG Notification Transport Capabilities draft-ietf-netconf-yp-transport-capabilities
YANG Library RFC 8525
Augmented-by Addition into the IETF-YANG-Library draft-ietf-netconf-yang-library-augmentation
Validating anydata in YANG Library context draft-netana-nmop-yang-anydata-validation
Encoding of Data Modeled with YANG in the CBOR RFC 9254
+------------------------------------------------------------+
| Data Storage |
+------------------------------------------------------------+
^
| (12) Ingest Data
| According to Schema
+------------------------------------------------------------+
| Data Consumer |
+------------------------------------------------------------+
| ^ ^
(10) Get | | | (9) Validate
Schema | | | Serialized Message
| | | Schema on Consumer
| | +--------------------+
| | | Message |
| | | Broker |
| | +--------------------+
| | ^
| | | (8) Serialize
| | (11) Issue | YANG-Push Message
| | Schema | annotated Schema
v | (6) Post | ID on Producer
+--------------------+ Schema +--------------------+
| YANG | <--------------- | Data Collection |
| Schema Registry | ---------------> | YANG-Push Receiver |
+--------------------+ (7) Issue +--------------------+
| Schema ID | ^ (3) Receive
| | | YANG-Push
v (4) Discover | | Subscription
+--------------------+ Schema | | Start Message
| Stream | Dependencies | | ^
| Catalog | and Obtain | | | (5) Publish
+--------------------+ Schemas | | | YANG-Push
| | | Message
| | | with
(1) Discover | | | Subscriber
Notification v | | ID
+--------------------+ Capabilities +--------------------+
| Manage YANG-Push | ---------------> | Network Node |
| Subscription | ---------------> | YANG-Push Publisher|
+--------------------+ (2) Subscribe +--------------------+

## Slide 5: Pmacct – Telemetry Message Support
yanglint-devel -i -t ext yang-modules/ietf-subscribed-notifications.yang yang-modules/ietf-yang-push-revision.yang yang-modules/ietf-yang-push.yang yang-modules/ietf-datastores.yang yang-modules/ietf-udp-notif-transport.yang yang-modules/ietf-yang-push-telemetry-message.yang yang-modules/ietf-telemetry-message.yang yang-modules/ietf-yang-types.yang yang-modules/ietf-yang-revisions.yang yang-modules/ietf-yang-semver.yang yang-modules/ietf-yang-structure-ext.yang yang-modules/ietf-yp-notification.yang yang-modules/ietf-inet-types.yang yang-modules/ietf-yang-types.yang yp210-subscription-started2.json -f json -k ietf-telemetry-message:structure:message
{
"ietf-telemetry-message:message": {
"telemetry-message-metadata": {
"collection-timestamp": "2025-01-01T01:00:30+01:00",
"notification-event": "log",
"session-protocol": "yang-push",
"export-address": "71.19.157.107",
"export-port": 31513
},
"data-collection-manifest": {
"name": "default",
"vendor": "pmacct",
"software-version": "1.7.10-git",
"software-flavor": "20251029-0 (7c22e2cf)"
},
"network-operator-metadata": {
"labels": [
{
"name": "seq",
"string-value": "1"
},
{
"name": "serialization",
"string-value": "json"
}
]
},
"payload": {
"ietf-yp-notification:envelope": {
"event-time": "2025-07-18T09:50:49.505Z",
"hostname": "ipf-zbl1327-r-daisy-91",
"sequence-number": 0,
"contents": {
"ietf-subscribed-notifications:subscription-started": {
"id": 210,
"ietf-yang-push:datastore": "ietf-datastores:operational",
"ietf-yang-push:datastore-xpath-filter": "openconfig-interfaces:interfaces/interface/state/counters",
"transport": "ietf-udp-notif-transport:udp-notif",
"ietf-yang-push-revision:module-version": [
{
"module-name": "openconfig-interfaces",
"revision": "2022-10-25"
}
],
"ietf-yang-push-revision:yang-library-content-id": "6d13bafd8fd1dc21aa8932d1199b369794881393",
"encoding": "encode-json",
"ietf-yang-push:periodic": {
"period": 3000,
"anchor-time": "2025-01-01T00:00:30+00:00"
}
}
}
}
}
}
}
draft-ietf-nmop-message-broker-telemetry-message support has been implemented in Pmacct for IETF 124 hackathon.
Libyang supports YANG data structures as of RFC 8791 as of version 4.0.14. This came as improvement from the IETF 123 YANG-Push validation activities.
NMOP & NETCONF WG

## Slide 6: Pmacct – Anydata to be valid I-JSON
Section 5.5 of RFC 7951 describes that an anydata YANG data node needs to be a valid I-JSON.
Since anydata-values andydata node contains the value "3" instead, yanglint is failing YANG validation.
NMOP & NETCONF WG
yanglint-devel -i -t ext yang-modules/ietf-subscribed-notifications.yang yang-modules/ietf-yang-push-revision.yang yang-modules/ietf-yang-push.yang yang-modules/ietf-datastores.yang yang-modules/ietf-udp-notif-transport.yang yang-modules/ietf-yang-push-telemetry-message.yang yang-modules/ietf-telemetry-message.yang yang-modules/ietf-yang-types.yang yang-modules/ietf-yang-revisions.yang yang-modules/ietf-yang-semver.yang yang-modules/ietf-yang-structure-ext.yang yang-modules/ietf-yp-notification.yang yang-modules/ietf-inet-types.yang yang-modules/ietf-yang-types.yang yp210-subscription-started.json -f json -k ietf-telemetry-message:structure:message
libyang err : Expecting JSON name/object but anydata "anydata-values" is represented in input data as name/number. (/ietf-telemetry-message:message/network-operator-metadata/labels[name='seq']) (line 41)
YANGLINT[E]: Parsing of extension data failed.
YANGLINT[E]: Failed to parse input data file "yp210-subscription-started.json".
"network-operator-metadata": {
"labels": [
{
"name": "seq",
"anydata-values": 3
},

## Slide 7: Pmacct – Typedef date-and-time Compliance
yanglint-devel -i -t ext yang-modules/ietf-subscribed-notifications.yang yang-modules/ietf-yang-push-revision.yang yang-modules/ietf-yang-push.yang yang-modules/ietf-datastores.yang yang-modules/ietf-udp-notif-transport.yang yang-modules/ietf-yang-push-telemetry-message.yang yang-modules/ietf-telemetry-message.yang yang-modules/ietf-yang-types.yang yang-modules/ietf-yang-revisions.yang yang-modules/ietf-yang-semver.yang yang-modules/ietf-yang-structure-ext.yang yang-modules/ietf-yp-notification.yang yang-modules/ietf-inet-types.yang yang-modules/ietf-yang-types.yang yp210-subscription-started1.json -f json -k ietf-telemetry-message:structure:message
libyang err : Invalid date-and-time timezone hour "",
"export-address": "71.19.157.107",
"export-port": 31513
}
}
}
".
libyang err : Invalid date-and-time timezone hour "",
"export-address": "71.19.157.107",
"export-port": 31513
}
}
}
". (/ietf-telemetry-message:message/telemetry-message-metadata/collection-timestamp) (line 51)
YANGLINT[E]: Parsing of extension data failed.
YANGLINT[E]: Failed to parse input data file "yp210-subscription-started1.json".
With Section 2.2 of RFC 9557 IETF updated RFC 3339 on timestamping semantics. draft-ietf-netmod-rfc6991-bis mirrors this in typedef date-and-time.
Pmacct needs to update collection-timestamp value to match typedef date-and-time schema.
NMOP & NETCONF WG

## Slide 8: Pmacct – Encoding value Namespace missing
yanglint-devel -i -t ext yang-modules/ietf-yang-push.yang yang-modules/ietf-yp-observation.yang yang-modules/openconfig-interfaces.yang yang-modules/Cisco-IOS-XR-openconfig-interfaces-stats-ext.yang yang-modules/ietf-yang-push-telemetry-message.yang yang-modules/ietf-telemetry-message.yang yang-modules/ietf-yang-types.yang yang-modules/ietf-yang-revisions.yang yang-modules/ietf-yang-semver.yang yang-modules/ietf-yang-structure-ext.yang yang-modules/ietf-yp-notification.yang yang-modules/ietf-inet-types.yang yang-modules/ietf-yang-types.yang yang-modules/ietf-udp-notif-transport.yang yp210-push-update1.json -f json -k ietf-telemetry-message:structure:message
libyang err : Invalid identityref "encode-json" value - identity not found in module "ietf-yang-push-telemetry-message". (/ietf-telemetry-message:message/telemetry-message-metadata/ietf-yang-push-telemetry-message:yang-push-subscription/encoding) (line 1333)
YANGLINT[E]: Parsing of extension data failed.
YANGLINT[E]: Failed to parse input data file "yp210-push-update1.json".
NMOP & NETCONF WG
"telemetry-message-metadata": {
"ietf-yang-push-telemetry-message:yang-push-subscription": {
"id": 210,
"transport": "ietf-udp-notif-transport:udp-notif",
"encoding": "encode-json",
}
}

## Slide 9: NetGauze – Telemetry Message Support
yanglint-devel -i -t ext yang-modules/ietf-subscribed-notifications.yang yang-modules/ietf-yang-push-revision.yang yang-modules/ietf-yang-push.yang yang-modules/ietf-datastores.yang yang-modules/ietf-udp-notif-transport.yang yang-modules/ietf-yang-push-telemetry-message.yang yang-modules/ietf-telemetry-message.yang yang-modules/ietf-yang-types.yang yang-modules/ietf-yang-revisions.yang yang-modules/ietf-yang-semver.yang yang-modules/ietf-yang-structure-ext.yang yang-modules/ietf-yp-notification.yang yang-modules/ietf-inet-types.yang yang-modules/ietf-yang-types.yang yp210-subscription-started4.json -f json -k ietf-telemetry-message:structure:message
{
"ietf-telemetry-message:message": {
"telemetry-message-metadata": {
"node-export-timestamp": "2025-07-18T11:50:49.505+02:00",
"collection-timestamp": "2025-07-18T11:50:49.503566119+02:00",
"notification-event": "log",
"session-protocol": "yang-push",
"export-address": "203.0.113.91",
"export-port": 31513,
"ietf-yang-push-telemetry-message:yang-push-subscription": {
"id": 210,
"xpath-filter": "openconfig-interfaces:interfaces/interface/state/counters",
"datastore": "ietf-datastores:operational",
"transport": "ietf-udp-notif-transport:udp-notif",
"encoding": "ietf-subscribed-notifications:encode-json",
"periodic": {
"period": 3000,
"anchor-time": "2025-01-01T01:00:30+01:00"
},
"yang-library-content-id": "6d13bafd8fd1dc21aa8932d1199b369794881393"
}
},
"data-collection-manifest": {
"name": "netgauze-yang-push@ietf-col-left01",
"vendor": "NetGauze",
"software-version": "0.7.0 (cba5eb90)",
"software-flavor": "release",
"os-version": "8.10",
"os-type": "Red Hat Enterprise Linux"
},
"network-operator-metadata": {
"labels": [
{
"name": "nkey",
"string-value": "unknown"
},
{
"name": "pkey",
"string-value": "unknown"
}
]
},
"payload": {
"ietf-yp-notification:envelope": {
"contents": {
"ietf-subscribed-notifications:subscription-started": {
"encoding": "ietf-subscribed-notifications:encode-json",
"id": 210,
"ietf-yang-push-revision:module-version": [
{
"module-name": "openconfig-interfaces",
"revision": "2022-10-25"
}
],
"ietf-yang-push-revision:yang-library-content-id": "6d13bafd8fd1dc21aa8932d1199b369794881393",
"ietf-yang-push:datastore": "ietf-datastores:operational",
"ietf-yang-push:datastore-xpath-filter": "openconfig-interfaces:interfaces/interface/state/counters",
"ietf-yang-push:periodic": {
"anchor-time": "2025-01-01T00:00:30Z",
"period": 3000
},
"transport": "ietf-udp-notif-transport:udp-notif"
}
},
"event-time": "2025-07-18T09:50:49.505Z",
"hostname": "ipf-zbl1327-r-daisy-91",
"sequence-number": 0
}
}
}
}
draft-ietf-nmop-message-broker-telemetry-message support has been implemented in Netgauze for IETF 123 hackathon.
Libyang supports YANG data structures as of RFC 8791 as of version 4.0.14. This came as improvement from the IETF 123 YANG-Push validation activities.
NMOP & NETCONF WG

## Slide 10: Next Steps from IETF 123 Hackathon…
Yanglint, fix YANG extension's structure support
Pmacct supporting Network Telemetry Message
YANG schema registry supporting YANG features
NetGauze supporting
  netconf <get> to obtain YANG library content,
  YANG validation for YANG-Push notifications,
  YANG schema registration.
NMOP & NETCONF WG

## Slide 11: Next Steps for IETF 125 Hackathon…
Yanglint, misses anydata validation support within YANG structures
Pmacct corrects collection-timestamp to be typedef date-and-time compliant.
Pmacct corrects encoding value to include ietf-subscribed-notifications namespace in JSON encoding.
Pmacct corrects network-operator-metadata/labels/anydata-values anydata statement to be valid I-JSON.
YANG schema registry supporting YANG features
NetGauze supporting
  netconf <get> to obtain YANG library content,
  YANG validation for YANG-Push notifications,
  YANG schema registration.
NMOP & NETCONF WG

## Slide 12: Thanks to…
Paolo Lucente – Pmacct
Maxence Younsi – INSA Lyon
Reshad Rahman - Equinix
Rob Wilton – Cisco
Dan Voyer – Cisco
Holger Keller – DT
Nils Warnke – DT
Benoit Claise - Everything OPS SRL
Yannick Buchs – Swisscom
Ahmed Elhassany – Swisscom
Thomas Graf – Swisscom
NMOP & NETCONF WG
Want to to know more than join us at…
NMOP on Monday 14:30-16:30 at Viger for Message Broker, Telemetry Message and Message Key.
NMOP on Wednesday 14:30 – 15:30 at Agora for more on Telemetry Message integration and validation.
NETMOD on Friday 09:30 – 11:00 at Van Horne for more on YANG anydata validation.