## Slide 1: SRv6 On-Path Delay Measurement with Anomaly Detection OPSAWG WG
IETF 116
March 25-26th, 2023
Hackathon

## Slide 2: Hackathon - Plan
Establish multivendor SRv6 network topology with network telemetry data collection and data processing pipeline.
Validate and visualize two IPFIX implementations of draft-ietf-opsawg-ipfix-srv6-srh (AD review) and draft-ietf-opsawg-ipfix-on-path-telemetry in FD.io VPP and on Huawei VRP.
Calculate PathDelayMeanDeltaMicroseconds by dividing PathDelaySumDeltaMicroseconds by packetDeltaCount in pmacct data collection
Extend Network Anomaly Detection to recognize on-path delay increase and include delay in Max Concern Score calculation.

## Slide 3: Hackathon – Software
Software
Huawei Versatile Routing Platform Software Version 8.220
VPP extended by INSA Lyon
Wireshark IPFIX dissector for packet analysis
pmacct nfacctd for IPFIX and BMP data collection
Confluent Apache Kafka as message broker
Apache Druid as timeseries DB
Imply Pivot as user interface

## Slide 4: Hackathon – Network (1/2)
SRv6 network topology with two vendors and IPFIX data processing pipeline.
Huawei with four P and two PE nodes exposing SRH provider data-plane draft-ietf-opsawg-ipfix-srv6-srh and on-path delay as described in draft-ietf-opsawg-ipfix-on-path-telemetry.
Cisco with two PE nodes exposing customer data-plane.

## Slide 5: Hackathon – Network (2/2)
FD.io VPP Open Source Code published: https://github.com/network-analytics/vpp-srh-onpath-telemetry

## Slide 6
Shows SRv6 SID list change of the traffic engineered paths.
Shows on which node how much on-path delay was being measured.
Shows the BGP update/withdrawals from the topology change.
Shows that Network Anomaly Detection detects the topology and delay change and the Max Concern Score calculation.
1
2
3
4
Visualization & Conclusion

## Slide 7
Pmacct Integration
{
"event_type": "purge",
"peer_ip_src": "33.33.33.33",
"ip_src": "2001:f4::1",
"ip_dst": "2001:f4::1",
"srv6_seg_ipv6_list": ["c4::6-0", "c2::-1"],
"packets": 20, "bytes": 10560, "PathDelayMean": 120,
}
IPFIX packet
JSON

## Slide 8: What we learned (again)
Good
  Preparation and good team setup is gold.
  As always… the beers were most welcome!
Surprise
  Yuta and his colleagues joining our table and implementing draft-ietf-opsawg-ipfix-srv6-srh in XDP/DPDK.

## Slide 9: Thanks to…
Alex Huang Feng – INSA
Severin Dellsperger - OST University (remote)
Camilo Cardona – NTT
Paolo Lucente – NTT
Benoit Claise – Huawei
Jean Quilbeuf - Huawei
Olga Havel – Huawei
Wanting Du – Swisscom (remote)
Yannick Buchs – Swisscom (remote)
Marco Tollini - Swisscom
Thomas Graf - Swisscom
….and Huawei, INSA Lyon and Pmacct for the network environment, software and test cases.