## Slide 1
UDP-based Transport for Configured Subscriptions draft-ietf-netconf-udp-notif-11
UDP-based protocol for YANG notifications
to collect data from networking devices
G. Zheng, Huawei T. Zhou, Huawei
T. Graf, Swisscom
P. Francois, INSA-Lyon
A. Huang Feng, INSA-Lyon
Paolo Lucente, NTT
26. October 2023

## Slide 2: UDP-based Transport for Configured Subscriptions Discussions from the ML
Thanks Jurgen Schonwalder, Andy Bierman, Hannes Tschofenig, Benoit Claise and Kent Watsen for the discussions on the ML
ISSUE 1: There are concerns about packet loss within the UDP transport
ISSUE 2: Why segmentation cannot be implemented at lower level (IP level)?
ISSUE 3: Header version number has not pointer to the IANA registry
ISSUE 4: Other editorial feedback
Notes: - Concerns about the segmentation design, given it is UDP, a loss of a packet makes the discard about the whole message (Hannes Tschofenig) --> defining segmentation here because of RFC8085: (An UDP application SHOULD NOT send UDP datagrams that result in IP packets that exceed the Maximum Transmission Unit (MTU) along the path to the destination)
- Jurgen Schonwalder --> Concerns about the probability of UDP packet loss
- Jurgen Schonwalder --> where is the performance impact? Can't 2023 linecards manage TCP?
- Andy --> narrow the scope of the draft to "small" messages
- Jurgen Schonwalder --> private encoding a bit overengineered?
- Jurgen Schonwalder --> 3-bit Ver field not pointing to the IANA [addressed]
- Hannes --> packet loss is negleactable, need to be explicit in the draft
- Jurgen --> which performance issues we are trying to tackle? not explicit
- Kent support the work for sending the telemetry data to the same rack
- Andy --> on-change notifications should be with TCP

## Slide 3: UDP-based Transport for Configured Subscriptions ISSUE 1: There are concerns about packet loss within the UDP transport
Concerns about packet loss using UDP transport
→ UDP-notif is to be used with small messages; for large messages, HTTPS-notif should be used
→ There is a statement in Applicability Section stating that is to be used when the packet loss is not a concern.
→ “on-change” notifications where the message cannot be lost, reliable transport MUST be used.
Section 5. Applicability
Notes: - Concerns about the segmentation design, given it is UDP, a loss of a packet makes the discard about the whole message (Hannes Tschofenig) --> defining segmentation here because of RFC8085: (An UDP application SHOULD NOT send UDP datagrams that result in IP packets that exceed the Maximum Transmission Unit (MTU) along the path to the destination)
- Jurgen Schonwalder --> Concerns about the probability of UDP packet loss
- Jurgen Schonwalder --> where is the performance impact? Can't 2023 linecards manage TCP?
- Andy --> narrow the scope of the draft to "small" messages
- Jurgen Schonwalder --> private encoding a bit overengineered?
- Jurgen Schonwalder --> 3-bit Ver field not pointing to the IANA [addressed]
- Hannes --> packet loss is negleactable, need to be explicit in the draft
- Jurgen --> which performance issues we are trying to tackle? not explicit
- Kent support the work for sending the telemetry data to the same rack
- Andy --> on-change notifications should be with TCP

## Slide 4: UDP-based Transport for Configured Subscriptions ISSUE 2: Why segmentation cannot be implemented at lower level?
Segmentation option is similar to IP fragmentation, why there is a need to have this approach at UDP-notif level?
→ RFC8085 (UDP Usage Guidelines) states that “an UDP application SHOULD NOT send UDP datagrams that result in IP packets that exceeds the MTU”
→ Performance tests from Hackathon 110: big drop of performance when IP fragmentation happens in Linux
→ We have completely aligned the draft with RFC8085 (UDP Usage Guidelines)
Notes: - Concerns about the segmentation design, given it is UDP, a loss of a packet makes the discard about the whole message (Hannes Tschofenig) --> defining segmentation here because of RFC8085: (An UDP application SHOULD NOT send UDP datagrams that result in IP packets that exceed the Maximum Transmission Unit (MTU) along the path to the destination)
- Jurgen Schonwalder --> Concerns about the probability of UDP packet loss
- Jurgen Schonwalder --> where is the performance impact? Can't 2023 linecards manage TCP?
- Andy --> narrow the scope of the draft to "small" messages
- Jurgen Schonwalder --> private encoding a bit overengineered?
- Jurgen Schonwalder --> 3-bit Ver field not pointing to the IANA [addressed]
- Hannes --> packet loss is negleactable, need to be explicit in the draft
- Jurgen --> which performance issues we are trying to tackle? not explicit
- Kent support the work for sending the telemetry data to the same rack
- Andy --> on-change notifications should be with TCP

## Slide 5: UDP-based Transport for Configured Subscriptions ISSUE 3: Header version number has not pointer to the IANA registry
Ver (protocol header) definition and IANA registry are not aligned
Notes: - Concerns about the segmentation design, given it is UDP, a loss of a packet makes the discard about the whole message (Hannes Tschofenig) --> defining segmentation here because of RFC8085: (An UDP application SHOULD NOT send UDP datagrams that result in IP packets that exceed the Maximum Transmission Unit (MTU) along the path to the destination)
- Jurgen Schonwalder --> Concerns about the probability of UDP packet loss
- Jurgen Schonwalder --> where is the performance impact? Can't 2023 linecards manage TCP?
- Andy --> narrow the scope of the draft to "small" messages
- Jurgen Schonwalder --> private encoding a bit overengineered?
- Jurgen Schonwalder --> 3-bit Ver field not pointing to the IANA [addressed]
- Hannes --> packet loss is negleactable, need to be explicit in the draft
- Jurgen --> which performance issues we are trying to tackle? not explicit
- Kent support the work for sending the telemetry data to the same rack
- Andy --> on-change notifications should be with TCP

## Slide 6: UDP-based Transport for Configured Subscriptions ISSUE 4: Editorial changes based on feedback from the ML
Message length definition clarified
  Message length is the UDP datagram length and not the message length when it is segmented
“Observation Domain ID” has been changed to “Message Publisher ID”
  Aligned with latest update in terminology section of draft-ietf-netconf-distributed-notif-08
Editorial changes on DTLS section stating that we are not extending DTLS 1.3
(feedback from Hannes Tschofenig)
Notes: - Concerns about the segmentation design, given it is UDP, a loss of a packet makes the discard about the whole message (Hannes Tschofenig) --> defining segmentation here because of RFC8085: (An UDP application SHOULD NOT send UDP datagrams that result in IP packets that exceed the Maximum Transmission Unit (MTU) along the path to the destination)
- Jurgen Schonwalder --> Concerns about the probability of UDP packet loss
- Jurgen Schonwalder --> where is the performance impact? Can't 2023 linecards manage TCP?
- Andy --> narrow the scope of the draft to "small" messages
- Jurgen Schonwalder --> private encoding a bit overengineered?
- Jurgen Schonwalder --> 3-bit Ver field not pointing to the IANA [addressed]
- Hannes --> packet loss is negleactable, need to be explicit in the draft
- Jurgen --> which performance issues we are trying to tackle? not explicit
- Kent support the work for sending the telemetry data to the same rack
- Andy --> on-change notifications should be with TCP

## Slide 7: UDP-based Transport for Configured Subscriptions Next Steps
Requesting feedback from the working group and suggest that the netconf chairs reach out to the Transport Area Directorate (https://datatracker.ietf.org/group/tsvdir/email/) next and request an early review before the document is moving forward to working group last call.
Open points to be addressed next
  Externalize generic YANG module for UDP clients
→ draft-ahuang-netconf-udp-client-server-00 has been submitted