## Slide 1
Validate anydata with YANG Library context
draft-netana-nmop-yang-anydata-validation
ahmed.elhassany@swisscom.com
thomas.graf@swisscom.com
07. Nov. 2025

## Slide 2: Problem statement
Users cannot validate the YANG data semantics if data is located under anydata subtree.
For example, if a router is sending negative values for counter types.
{
"ietf-yang-push:push-update": {
"id": 89,
"datastore-contents": {
"ietf-interfaces:interfaces": {
"interface": [
{
"name": "eth0",
"statistics": {"in-octets": -10}
}]
}}
}
}
Router is sending negative value for yang:counter64

## Slide 3: Survey of existing use of “anydata”
Operations on a YANG datastore
  A NETCONF subtree filter to select a subtree on an instantiated YANG data tree; RFC 8526, RFC 9144, and RFC 8641.
  The output of a subtree filter or XPATH; RFC 8526, RFC 9144, and RFC 8641.
  To represent edit operations on YANG data tree with YANG Patch; RFC 8072.
Represent a YANG-like data tree (RFCs were not very clear)
  Subscribed notifications in RFC 8639.
  Error information in RESTCONF RFC 8040.

## Slide 4: The goals of this document
Provide optional way for Network Operators to check the validity of the YANG data at scale.
YANG data consumer can choose to enable or disable stricter validation of anydata subtrees.
Data marked as invalid are processed by a different pipeline than the normal one (e.g., logging for further analysis) such that the main business logic is never impacted with misbehaving YANG producers (e.g., integer overflow bug to produce negative counter values).

## Slide 5: YANG Library look up
The namespace of the encoded data nodes under anydata can be looked up in a YANG Library context.
This approach DOES NOT restrict what a producer can put under anydata subtree.
It only checks whatever subtree under the anydata have a corresponding schema and it is valid according to it.
{
"ietf-yang-library:yang-library": {
"module-set": [
{
"name": "complete",
"module": [
{
"name": "yang",
"revision": "2022-06-16",
"namespace": "urn:ietf:params:xml:ns:yang:1"
},
{
"name": "ietf-interfaces",
"revision": "2018-02-20",
"namespace": "urn:ietf:params:xml:ns:yang:ietf-interfaces",
"location": ["file://ietf-interfaces@2018-02-20.yang"],
"feature": [
"arbitrary-names",
"pre-provisioning",
"if-mib"
]
},
…

## Slide 6: Changes since IETF 123
Clarify the problem statement and the impact of having unvalidated anydata subtrees.
A survey of existing usage of anydata within IETF documents.

## Slide 7: Implementation
Current libyang implementation disables strict parsing in anydata subtree. Implementing this document would require to change this behavior with an optional flag and use strict validation always.
diff --git a/src/parser_xml.c b/src/parser_xml.c
index 5d97c8e49..6938d3712 100644
--- a/src/parser_xml.c
+++ b/src/parser_xml.c
@@ -931,7 +931,7 @@ lydxml_subtree_any(struct lyd_xml_ctx *lydctx, const struct lysc_node *snode, co
LY_CHECK_ERR_GOTO(r, rc = r, cleanup);
/* update options so that generic data can be parsed */
- lydctx->parse_opts &= ~LYD_PARSE_STRICT;
+ //lydctx->parse_opts &= ~LYD_PARSE_STRICT;
lydctx->parse_opts |= LYD_PARSE_OPAQ | (ext ? LYD_PARSE_ONLY : 0);
lydctx->int_opts |= LYD_INTOPT_ANY | LYD_INTOPT_WITH_SIBLINGS;

## Slide 8: Question and next steps
We clarified with NMOP, NETMOD chairs and Mahesh as OPS Area AD which working group would apply. Since the document proposes an update to RFC 7950, NETMOD would be the target working group according to Mahesh. -> Therefore, we request NETMOD working group adoption
Extend the libyang implementation to support complete validation.
Push changes to libyang and make them accessible via yanglint.

## Slide 9: Where anydata is currently used? incomplete list
  RFC 8342: ietf-netconf-nmda
  RFC 9144: ietf-nmda-compare
  RFC 8040: ietf-restconf
  RFC 8639: ietf-subscribed-notifications
  RFC 9195: ietf-yang-instance-data
  RFC 8072: ietf-yang-patch
  RFC 8641: ietf-yang-push
  RFC 8532: ietf-connectionless-oam (uses yang mount)
  RFC 8791: any YANG data structure is encoded the same way as anydata node.

## Slide 10: Context
RFC 7950: The YANG 1.1 Data Modeling Language
  The "anydata" statement is used to represent an unknown set of nodes that can be modeled with YANG, except anyxml, but for which the data model is not known at module design time. It is possible for the data model, though not required, for anydata content to become known through protocol signaling or other means that are outside the scope of this document.

## Slide 11: RFC 8525 YANG Library
  YANG Library provides information about the YANG modules, datastores, and datastore schemas used by a network management server.
{
"ietf-yang-library:yang-library": {
"module-set": [
{
"name": "complete",
"module": [
{
"name": "ietf-interfaces",
"revision": "2018-02-20",
"namespace": "urn:ietf:params:xml:ns:yang:ietf-interfaces",
"location": ["file://ietf-interfaces@2018-02-20.yang"],
"feature": [
"arbitrary-names",
"pre-provisioning",
"if-mib"
]
},
…

## Slide 12: YANG Data encodings
{
"ietf-yang-push:push-update": {
"id": 89,
"datastore-contents": {
"ietf-interfaces:interfaces": {
"interface": [
{
"name": "eth0",
"oper-status": "down"
}]
}}
}
}
<push-update xmlns="urn:ietf:params:xml:ns:yang:ietf-yang-push">
<id>89</id>
<datastore-contents>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">eth0</name>
<oper-status>down</oper-status>
</interface>
</interfaces>
</datastore-contents>
</push-update>
YANG Data JSON & XML encodings always contain full namespace information to identify the relevant YANG module.