## Slide 1
Support of Versioning in YANG Notifications Subscription draft-ietf-netconf-yang-notifications-versioning-03
Adds semantics to the subscription process and notification message to enable automated data mesh integration
thomas.graf@swisscom.com
benoit.claise@huawei.com
alex.huang-feng@insa-lyon.fr
27. October 2023

## Slide 2: Extend Datastore Selection and Subscription State Change Notifications with module name, revision and revision-label
module: ietf-yang-push-revision
augment /sn:establish-subscription/sn:input/sn:target/sn:stream
/sn:stream-filter/sn:within-subscription:
+-- module-version* [module-name]
+-- module-name yang:yang-identifier
+-- revision? rev:revision-date-or-label
+-- revision-label? ysver:version
augment /sn:establish-subscription/sn:input/sn:target/yp:datastore
/yp:selection-filter/yp:within-subscription:
+-- module-version* [module-name]
+-- module-name yang:yang-identifier
+-- revision? rev:revision-date-or-label
+-- revision-label? ysver:version
augment /sn:subscription-started/sn:target/sn:stream
/sn:stream-filter/sn:within-subscription:
+--ro module-version* [module-name]
+--ro module-name yang:yang-identifier
+--ro revision rev:revision-date-or-label
+--ro revision-label? ysver:version
augment /sn:subscription-started/sn:target/yp:datastore
/yp:selection-filter/yp:within-subscription:
+--ro module-version* [module-name]
+--ro module-name yang:yang-identifier
+--ro revision rev:revision-date-or-label
+--ro revision-label? ysver:version
Network operators need to control semantics in its data processing pipeline. That includes YANG push.
This is today only possible during YANG push subscription but not when nodes are being upgraded or messages are being published for configured subscription.
draft-ietf-netconf-yang-notifications-versioning extends the YANG push subscription and publishing mechanism defined in RFC8641:
  By adding the ability to subscribe to a specific revision or latest-compatible-semversion of one or more yang modules.
  By extending the YANG push Subscription State Change Notifications Message so that the YANG push receiver learns beside the xpath and the sub-tree filter also the yang module name, revision and revision-label.
{
"ietf-restconf:notification" : {
"eventTime": "2023-01-03T10:00:00Z",
"ietf-subscribed-notifications:subscription-modified": {
"id": 101,
"stream-xpath-filter": "/ietf-interfaces:interfaces",
"stream": "NETCONF",
"ietf-yang-push-revision:module-version": [{
"module-name": "ietf-interfaces"
"revision": "2014-05-08",
"revision-label": "1.0.0",
}],
}
}
}

## Slide 3: Versioning in YANG Notifications Subscription Status and Next Steps
Feedback from Qiufang and Rob at IETF 117
  Extend the Datastore Selection section now describes error handling. Error identities with examples for revision-unsupported, revision-label-unsupported and incompatible-revision-and-revision-label added.
  Operational Section describes YANG package context; It offers a complementary information by describing how one specific YANG module revision is part of a set of YANG modules.
All addressed in -03 revision -> Requesting feedback and comments.
YANG @ Kafka side meeting today November 7th at 15:30 in room Palmovka 1/2. -> Updates on semantic YANG Push message validation outcome from hackathon activity
thomas.graf@swisscom.com
benoit.claise@huawei.com
alex.huang-feng@insa-lyon.fr
27. October 2023

## Slide 4
Backup

## Slide 5
Data Mesh is a big data architecture where different domains can exchange data with a bounded context and SLO's are defined in Data Products. Same principle as in networks.
Semantics are needed to describe the data. A gauge32 is not the same as counter32. Values can increase or decrease. Needs monotonic increasing counter normalization or not.
Versioning is needed to not only understand that the semantic has changed, but also wherever the new semantic is backward compatible or not. Preventing to break the data processing pipeline.
Hostname, publisher ID, sequence numbers and observation timestamping are needed to measure loss and delay for SLO's.
YANG push as defined in RFC8641 is missing hostname, sequence numbers, observation timestamping and versioning. draft-ahuang-netconf-notif-yang, draft-tgraf-netconf-notif-sequencing, draft-tgraf-netconf-yang-push-observation-time and draft-ietf-netconf-yang-notifications-versioning addresses this.
When Big Data and Network becomes one Marrying two messaging protocols