## Slide 1
Support of Hostname and Sequencing in YANG Notifications draft-tgraf-netconf-notif-sequencing-02
Adds sysName, messagePublisherId and sequenceNumber to identify from where the message was exported from
for automated data mesh integration
thomas.graf@swisscom.com
jean.quilbeuf@huawei.com alex.huang-feng@insa-lyon.fr
27. October 2023

## Slide 2: Extend Streaming Update Notifications with Hostname and Sequencing For push-update and push-change-update
module: ietf-notification
structure notification:
+-- eventTime yang:date-and-time
+-- inotifseq:sysName inet:host
+-- inotifseq:messagePublisherId uint32
+-- inotifseq:sequenceNumber yang:counter32
When the NETCONF event notification message is forwarded from the YANG push receiver to another system, such as a messaging system or a time series database where the message is stored, the transport context is lost since it is not part of the NETCONF event notification message metadata. Therefore, the downstream system is unable to associate the message to the publishing process (the exporting router), nor able to detect message loss or reordering.
draft-tgraf-netconf-notif-sequencing extends the NETCONF notification defined in RFC5277 with:
  sysName: Describes the hostname following the 'sysName' object definition in RFC1213 from where the message was published from.
  messagePublisherId: netconf-distributed-notif describes the ability to publish from network processors directly. With this identifier the publishing process from where the message was published from can be uniquely identified.
  sequenceNumber: Generates a unique sequence number as described in RFC9187 for each published message.
<notification xmlns="urn:ietf:params:xml:ns:netconf:notification:1.0">
<eventTime>2023-02-04T16:30:11.22Z</eventTime>
<sysName xmlns="urn:ietf:params:xml:ns:yang:ietf-notification-sequencing">
example-router
</sysName>
<messagePublisherId xmlns="urn:ietf:params:xml:ns:yang:ietf-notification-sequencing">
1
</messagePublisherId>
<sequenceNumber xmlns="urn:ietf:params:xml:ns:yang:ietf-notification-sequencing">
187653
</sequenceNumber>
<push-update xmlns="urn:ietf:params:xml:ns:yang:ietf-yang-push">
<id>1011</id>
<datastore-contents>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>eth0</name>
<oper-status>up</oper-status>
</interface>
</interfaces>
</datastore-contents>
</push-update>
</notification>

## Slide 3: Extend Streaming Update Notifications Status and Next Steps
Introduced at IETF 116
  Poll showed much interested in the NETCONF working group.
Updates introduced in -02
  Message Publisher ID terminology aligned with latest update in terminology section of draft-ietf-netconf-distributed-notif-08.
  No open points. Requesting to initiate working group adoption call.
YANG @ Kafka side meeting today November 7th at 15:30 in room Palmovka 1/2. -> Updates on semantic YANG Push message validation outcome from hackathon activity
thomas.graf@swisscom.com
jean.quilbeuf@huawei.com alex.huang-feng@insa-lyon.fr
27. October 2023

## Slide 4
Backup

## Slide 5
Data Mesh is a big data architecture where different domains can exchange data with a bounded context and SLO's are defined in Data Products. Same principle as in networks.
Semantics are needed to describe the data. A gauge32 is not the same as counter32. Values can increase or decrease. Needs monotonic increasing counter normalization or not.
Versioning is needed to not only understand that the semantic has changed, but also wherever the new semantic is backward compatible or not. Preventing to break the data processing pipeline.
Hostname, publisher ID, sequence numbers and observation timestamping are needed to measure loss and delay for SLO's.
YANG push as defined in RFC8641 is missing hostname, sequence numbers, observation timestamping and versioning. draft-ahuang-netconf-notif-yang, draft-tgraf-netconf-notif-sequencing, draft-tgraf-netconf-yang-push-observation-time and draft-ietf-netconf-yang-notifications-versioning addresses this.
When Big Data and Network becomes one Marrying two messaging protocols