## Slide 1
An Architecture for a Network Anomaly Detection Framework draft-netana-nmop-network-anomaly-architecture-00
Motivation and architecture of a Network Anomaly Detection Framework
and the relationships to other documents describing
network symptom semantics and network incident lifecycle
wanting.du@swisscom.com pierre.francois@insa-lyon.fr
thomas.graf@swisscom.com vincenzo.riccobene@huawei-partners.com alex.huang-feng@insa-lyon.fr
16. July 2024

## Slide 2: Data Mesh organizes Data in Organizations Enables Network Analytics use cases
Network Data Collection
Network Device Trend Detection
Verify, Troubleshoot and Notify
Closed Loop Operation
Network Anomaly Detection
Network Visualization
Network SLI and SLO
Alert
Postmortem
Operational Data
draft-netana-nmop-network-anomaly-semantics draft-netana-nmop-network-anomaly-lifecycle
RFC 8632
Analytical Data
Network Telemetry
RFC 9232
draft-netana-nmop-network-anomaly-architecture

## Slide 3: What to monitor Which metrics are collected
« Network operators connect customers in routing tables called Connectivity Services »
« Network Telemetry (RFC 9232) describes how to collect data from all 3 network planes efficiently »

## Slide 4: What does Network Anomaly Detection mean Monitor changes, called outliers, in networks
Network Anomaly Detection
For Connectivity Services, Network Anomaly Detection constantly monitors and detects any network or device topology change, along with their associated forwarding consequences for customers as outliers. Notifications are sent to the Network Operation Center before the customer is aware of service disruptions. It offers operational metrics for in-depth analysis, allowing to understand in which platform the problem originates and facilitates problem resolution.
Answers
What changed and when, on which connectivity service, and how does it impact the customers?
Focuses
Provides meaningful connectivity service impact information before customer is aware of and support in root-cause analysis.
Data Mesh
Consumes operational real-time Forwarding Plane, Control Plane and Management Plane metrics and produces analytical alerts.
Direction
From connectivity service to network platform.

## Slide 5: What our motivation is Automate learn and improve
From network incidents postmortems we network operators learn and improve so does network anomaly detection and supervised and semi-supervised machine learning.
The more network incidents are observed, the more we can improve. With more incidents the postmortem process needs be automated, let's get organized first by defining human and machine-readable metadata semantics and annotate operational and analytical data.
Let's get further organized by exchanging standardized labeled network incident data among network operators, vendors and academia to collaborate on academic research.
« The community working on Network Anomaly Detection is probably the only group wishing for more network incidents »

## Slide 6: Elements of the Architecture
Service Inventory contains list of the connectivity services.
Service Disruption Detection processes aggregated network data to decide whether a service is degraded or not.
Service Disruption Detection Configuration defines the set of approaches that need to be applied to perform SDD.
Operational Data Collection manages network telemetry subscriptions and transforms data into message broker.
Operational Data Aggregation produces data upon which detection of a service disruption can be performed.
Network Modeling establishes knowledge of network relationships.
Data Profiling categorizes nondeterministic customer related data.
Detection Strategies for a profile a detection strategy is defined.
Machine Learning is commonly used to detect outliers or anomalies.
Storage some algorithms may relay on historical (aggregated) operational data to detect anomalies.
Alerting consolidates analytical insights and notifies.
Postmortem refines and stores the network anomaly and symptom labels into the Label Store.
Replaying to validate refined anomaly and symptom labels, historical operational data is replayed.

## Slide 7: Semantic Metadata Annotation for Network Anomaly Detection draft-netana-nmop-network-anomaly-semantics
module: ietf-symptom-semantic-metadata
+--rw symptom
+--rw id? yang:uuid
+--rw event-id? yang:uuid
+--rw description? string
+--rw start-time? yang:date-and-time
+--rw end-time? yang:date-and-time
+--rw confidence-score? score
+--rw concern-score? score
+--rw tags* [key]
| +--rw key string
| +--rw value string
+--rw (pattern)?
| +--:(drop)
| | +--rw drop empty
| +--:(spike)
| | +--rw spike empty
| +--:(mean-shift)
| | +--rw mean-shift empty
| +--:(seasonality-shift)
| | +--rw seasonality-shift empty
| +--:(trend)
| | +--rw trend empty
| +--:(other)
| +--rw other string
+--rw annotator
+--rw (annotator-type)
| +--:(human)
| | +--rw human empty
| +--:(algorithm)
| +--rw algorithm empty
+--rw name? string
Symptom ID and description uniquely identifies the detected anomaly. Event ID, start/end-time and confidence/concern-score uniquely identifies the network event with its start and end time, how confident the system identified the anomaly and how concerned an operator should be.
Tags allows to add customer information.
Pattern describes the identified pattern of the anomaly.
Annotator Name, Type, describes wherever the anomaly was detected by a human or algorithm and uniquely identifies the system who/which detected.

## Slide 8: Experiment: Network Anomaly Lifecycle draft-netana-nmop-network-anomaly-lifecycle
Detection: The Network Anomaly Detection stage is about the continuous monitoring of the network through Network Telemetry [RFC9232] and the identification of symptoms.
Validation: Decides if the detected symptoms are signaling a real incident or if they are to be treated as false positives.
Refinement: Network operator performs detailed postmortem analysis of the network incident, collected Network Telemetry data and detected anomaly with the objective to identify useful adjustments in the Network Telemetry data collection and Anomaly Detection system.
« Network Anomaly Detection is an iterative process that requires continuous improvement »

## Slide 9: Experiment: Network Anomaly Lifecycle draft-netana-nmop-network-anomaly-lifecycle
module: ietf-network-anomaly-metadata
+--rw network-anomalies
+--rw network-anomaly* [id version]
+--rw id yang:uuid
+--rw version uint32
+--rw description? string
+--rw state identityref
+--rw annotator
| +--rw (annotator-type)
| | +--:(human)
| | | +--rw human empty
| | +--:(algorithm)
| | +--rw algorithm empty
| +--rw name? empty
+--rw symptoms* [symptom_id]
+--rw symptom_id yang:uuid
ID and Description uniquely identifies the detected network anomaly (as a container of symptoms).
Description and State provide general information regarding the anomaly and .
Annotator describes the entity that observed the network anomaly: this can be a human or an algorithm (anomaly detection system).
Symptoms provides a list of symptoms (based on ietf-symptom-metadata) that are part of this network anomaly.

## Slide 10: Experiment: Antagonist anomaly tagging on historical data
Goals:
Prove that YANG models contain all the necessary information
Validate models across a wide range of use-cases
Show interoperability between
Done so far:
Validation with real operational data (Cloud monitoring)
Validation with rule-based Network Anomaly Detector (SAIN RFC9417/RFC9418)
Validation with a ML-based Network Anomaly Detector (Autoencoder)
Add support for Re-training of ML-based models
Add partial support for Metadata Filtering and search
YANG model refinements to reflect the results of the coding
Automatic dashboard generation
Next Steps:
Improve scalability
Validate with Swisscom Data

## Slide 11: Swisscom - Cosmos Bright Lights PoC Summary After 20 Incidents and 18 Months Time
46
Falls Positive due to Apache Druid delayed ingestion
5
In Replay Incident Detected
Chart: 
| Realtime | Replay | Falls Delay | Falls Previous
Spalte1 | 7 | 3 | 11 | 3
15
In Near Real-Time Incident Detected
6
Falls Positive due to previous week data not comparable
72 Alert Notifications
Key Facts in V0 (2023-2024)
16 L3 VPNs proactively monitored.
Individual Service Disruption Detection rule accuracy is beyond 90%. Summed accuracy is beyond 95%.
Max Concern score ranged between 0.06 and 0.85. In average 0.46.
In 4 cases additional YANG, in 13 cases additional BMP, in 2 cases Netconf Transaction-ID and 1 case additional L2 IPFIX metrics would have helped to gain more visibility.
Key observability feature missing: BMP Local RIB with Path Marking.

## Slide 12: Swisscom - Cosmos Bright Lights PoC Detail Multiple Perspectives increases Accuracy
Key Improvements in V1 (2024)
>12000 L3 VPNs proactively monitored since June 2024.
Realtime Streaming eliminates delayed ingestion falls positives and scaling.
Improved profiling. Compares to multiple previous weeks and discard largest deviation eliminates falls positives. -> Work In progress
Key Improvements in V2 (2025)
Annotate operational and analytical Network Incident data for reproduction.
Enabling automated workflow. From PowerPoint slide decks to data driven actionable insights.
6
Three out of Six checks
3
One out of Six checks
Chart: 
| One | Two | Three | Four
Spalte1 | 3 | 8 | 6 | 2
2
Four out of Six checks
8
Two out of Six checks
20 Network Incidents

## Slide 13: An Architecture for a Network Anomaly Detection Framework Status, Summary and Next steps
Status of draft-netana-nmop-network-anomaly-architecture-00
Initial document published. Requesting feedback from the working group.
Status of draft-netana-nmop-network-anomaly-semantics-02 and draft-netana-nmop-network-anomaly-lifecycle-03
Referred to draft-netana-nmop-network-anomaly-architecture as the architecture document.
Change the term source to annotator and updated the YANG modules accordingly.
Added/updated terminology section with references to draft-ietf-nmop-terminology and draft-netana-nmop-network-anomaly-architecture.
Moved data mesh and outlier detection section to draft-netana-nmop-network-anomaly-architecture.
Next Steps
Request adoption for all 3 anomaly detection documents starting with draft-netana-nmop-network-anomaly-architecture-00.
NMOP interim meeting on September 11th proposal
  Network incident postmortem examples from Swisscom and Bell Canada
  Detailing documents, updates and hackathon experiment results

## Slide 14: Relevant Papers for more Details
Paper “Daisy: Practical Anomaly Detection in large BGP/MPLS and BGP/SRv6 VPN Networks” published at ACM/IRTF ANRW’23
San Francisco, USA (24 July 2023)
Open access: http://hal.science/hal-04307611
Paper “Practical Anomaly Detection in Internet Services: An ISP centric approach”
accepted at AnNet’24
(in conjunction with IEEE NOMS’24)
Seoul, Korea (6–10 May 2024)
[Will be presented as a poster the May 6th 2024]