## Slide 1
Support of Versioning in YANG Notifications Subscription draft-ietf-netconf-yang-notifications-versioning-05
Adds semantics to the subscription process and notification message to enable automated data mesh integration
thomas.graf@swisscom.com
benoit.claise@huawei.com
alex.huang-feng@insa-lyon.fr
12. July 2024

## Slide 2: Support of Versioning in YANG Notifications Subscription For subscription state change notification messages
module: ietf-yang-push-revision
augment /sn:establish-subscription/sn:input:
+---w module-version-config* [module-name]
+---w module-name yang:yang-identifier
+---w revision? rev:revision-date-or-label
+---w revision-label? ysver:version
augment /sn:subscription-started:
+--ro module-version* [module-name]
+--ro module-name yang:yang-identifier
+--ro revision rev:revision-date-or-label
+--ro revision-label? ysver:version
Network operators need to control semantics in its data processing pipeline. That includes YANG-Push.
This is today only possible during YANG-Push subscription but not when nodes are being upgraded or when messages are being published for configured subscription.
draft-ietf-netconf-yang-notifications-versioning extends the YANG push subscription and publishing mechanism defined in RFC 8641:
  By adding the ability to subscribe to a specific revision or latest-compatible-semversion of one or more yang modules.
  By extending the YANG push Subscription State Change Notifications Message so that the YANG push receiver learns beside the xpath and the sub-tree filter also the yang module name, revision and revision-label.
{
"ietf-notification:notification": {
"eventTime": "2023-03-25T08:30:11.22Z",
"ietf-notification-sequencing:sysName": "example-router",
"ietf-notification-sequencing:sequenceNumber": 1,
"ietf-subscribed-notification:subscription-started": {
"id": 6666,
"ietf-yang-push:datastore": "ietf-datastores:operational",
"ietf-yang-push:datastore-xpath-filter": "/if:interfaces",
"ietf-yang-push-revision:revision": "2014-05-08",
"ietf-yang-push-revision:module-name": "ietf-interfaces",
"ietf-yang-push-revision:revision-label": "",
"ietf-distributed-notif:message-observation-domain-id": [1,2],
"transport": "ietf-udp-notif-transport:udp-notif",
"encoding": "encode-json",
"ietf-yang-push:periodic": {
"ietf-yang-push:period": 100
}
}
}
}

## Slide 3: Support of Versioning in YANG Notifications Subscription draft-ietf-netconf-yang-notifications-versioning-04 - Status and Next Steps
Current Status
Resolved issue that within a "case" statement identifiers need to be unique.
Thanks to Jérémie Leska from 6Wind for reporting this issue.
Next Steps
Validate implementation at IETF 120 hackathon.
Requesting feedback from the netconf working group and YANG-Push implementers.

## Slide 4: YANG-Push Implementation Status IETF 120
 | 6WIND VSR | Huawei VRP | Cisco IOS XR
RFC 8641 YANG-Push | x | x | x
draft-ietf-netconf-udp-notif | x | x | 
draft-ietf-netconf-distributed-notif | x | x | 
draft-ietf-netconf-yang-notifications-versioning | x | x | 
draft-tgraf-netconf-notif-sequencing | x |  | 
draft-tgraf-netconf-yang-push-observation-time | x |  | 
RFC 7895 YANG Module Library |  | x | 
RFC 8525 YANG Library | x |  | x
draft-lincla-netconf-yang-library-augmentation |  |  | 

## Slide 5: Address YANG Specification and Integration Gaps Aiming for an automated data processing pipeline
YANG Specifications Gaps:
YANG model for NETCONF Event Notifications draft-ahuang-netconf-notif-yang
Validating anydata in YANG Library context draft-aelhassany-anydata-validation
YANG Integration Gaps:
Support of Network Observation Timestamping in YANG Notifications draft-tgraf-netconf-yang-push-observation-time
Support of Hostname and Sequencing in YANG Notifications draft-tgraf-netconf-notif-sequencing
Support of Versioning in YANG Notifications Subscription draft-ietf-netconf-yang-notifications-versioning
Augmented-by Addition into the IETF-YANG-Library draft-lincla-netconf-yang-library-augmentation
« Addressing those gaps are a prerequisite to enable an automated data processing chain as described in draft-ietf-nmop-yang-message-broker-integration. Please consider to attend IETF 120 NMOP working group session on Friday 13:00 – 15:00
or go onto the mailing list and contribute to the discussion. »